## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy
Abdullah Yasin Nur

## Slide 2: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
§5.1 Introduction

## Slide 3: Memory Hierarchy
L1/L2 Cache
Registers
Main Memory
Secondary Storage
Magnetic Tape
Typical Capacity
Typical Access Time
1 nanosecond
2 nanoseconds
10 – 100 nanoseconds
10 milliseconds
100 seconds
< 1 KB
32 KB/4 MB
1 – 16 GB
128 - 2000 GB
500 - 1000 GB
Recall

## Slide 4: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 5: Memory Hierarchy Levels
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 6: The Memory Hierarchy: Terminology
Block (or line): the minimum unit of information that is present (or not) in a cache
Hit Rate: the fraction of memory accesses found in a level of the memory hierarchy
  Hit Time: Time to access that level which consists of
    Time to access the block + Time to determine hit/miss
Miss Rate: the fraction of memory accesses not found in a level of the memory hierarchy  1 - (Hit Rate)
  Miss Penalty: Time to replace a block in that level with the corresponding block from a lower level which consists of
    Time to access the block in the lower level
    + Time to transmit that block to the level that experienced the miss
    + Time to insert the block in that level
    + Time to pass the block to the requestor
Hit Time << Miss Penalty

## Slide 7: Memory Technology
Static RAM (SRAM) e.g. Cache
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM) e.g. RAM
  50ns – 70ns, $20 – $75 per GB
Magnetic disk e.g. Harddisk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Fast access - Access time of SRAM
  Large Capacity - Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 8: SRAM Technology
Integrated circuits that are memory arrays with a single port
  Read or write
SRAMs use six to eight transistors per bit to prevent the information from being disturbed when read.
SRAM needs only minimal power to retrain the charge in standby mode.

## Slide 9: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back
    Performed on a DRAM “row”
Figure: Internal organization of a DRAM.
Modern DRAMs are organized in banks, typically 4 for DDR3.
Each bank consists of series of rows.
Notes: Sending a PRE (precharge) command opens or closes a bank. A row address is sent with an Act (activate), which causes the row to transfer to a buffer. When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3) or by specifying a block transfer and the starting address. Each command, as well as block transfers, is synchronized with a clock.

## Slide 10: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
Quad data rate (QDR) DRAM
  Separate DDR inputs and outputs
Self Study

## Slide 11: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50
Chart: 
| '80 | '83 | '85 | '89 | '92 | '96 | '98 | '00 | '04 | '07
Trac | 250 | 185 | 135 | 110 | 90 | 60 | 60 | 55 | 50 | 40
Tcac | 150 | 100 | 40 | 40 | 30 | 12 | 10 | 7 | 5 | 1.25
Ta2nrc
Acat2er
Ta2nrc  Total access time to a new row / column
Acat2er  Average column access time to existing row
ns 
Year 

## Slide 12: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth
  DIMMs (Dual Inline Memory Modules) contains 4 ~16 DRAMs, are organized to be 8 byte wide for servers.
Self Study

## Slide 13: Flash Storage
Electrically Erasable Programmable Read-only Memory (EEPROM)
Non-volatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)
§6.4 Flash Storage

## Slide 14: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks
Self Study

## Slide 15: Disk Storage
Nonvolatile, rotating magnetic storage
§6.3 Disk Storage

## Slide 16: Disk Storage
Consists of a collection of platters
  Rotate on a spindle at 5400 to 15000 revolutions per minute (rpm)
Track: concentric circles
  Tens of thousands of tracks pers surface.
  Each track divided into sectors that contain the information.
§6.3 Disk Storage

## Slide 17: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 18: Disk Sectors and Access
The operating system must direct the disk through a three stage process
Seek
Rotate
Disk access

## Slide 19: Disk Sectors and Access
Seek time
  Position the head over the proper track
  Disk manufacturers report minimum, maximum and average seek time in their manuals
  Average seek time is usually advertise as 3ms to 13ms.

## Slide 20: Disk Sectors and Access
Rotational delay
  Once the head has reached the correct track, we must wait for the desired sector to rotate under the read/write head.
  The average latency is halfway around the disk.
    Head can go both way
  The average rotational latency at 5400 RPM is
0.0056 seconds = 5.6 ms
RPM => Revolutions per minute

## Slide 21: Disk Sectors and Access
Disk access, transfer time
  The time to transfer a block of bits
Transfer rates in 2012 were between 100 and 200 MB/s
For a quick comparison between magnetic disk and DRAM
  DDR3 data transfer rates up to 6.4 GB/s
  DDR4 data transfer rates up to 25.6 GB/s

## Slide 22: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
  What is the time needed to transfer 512B?
Average read time (per sector)
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 23: Disk Performance Issues
Manufacturers quote average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Smart disk controller allocate physical sectors on disk
  Present logical sector interface to host
  SCSI, ATA, SATA
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay
Self Study

## Slide 24: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
  Locality of access
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches

## Slide 25: Cache Basics
Two questions to answer (in hardware):
  Q1: How do we know if a data item is in the cache?
  Q2: If it is, how do we find it?
Direct mapped
  Each memory block is mapped to exactly one block in the cache
    lots of lower level blocks must share blocks in the cache
  Address mapping (to answer Q2):
  (block address) modulo (# of blocks in the cache)
  Have a tag associated with each cache block that contains the address information (the upper portion of the address) required to identify the block (to answer Q1)

## Slide 26: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits
Notes: A direct-mapped cache with eight entries showing the addresses of memory words between 0 and 31 that map to the same cache locations. Because there are eight words in the cache, an address X maps to the direct-mapped cache word X modulo 8. That is, the low-order log2(8) = 3 bits are used as the cache index. Thus, addresses 00001two, 01001two, 10001two, and 11001two all map to entry 001two of the cache, while addresses 00101two, 01101two, 10101two, and 11101two all map to entry 101two of the cache.

## Slide 27: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 28: Cache Example

## Slide 29: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 30: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 31: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 32: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 33: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 34: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 35: Measuring the Cache
2m
(2m+2
2m
2m+5 bits
bits

## Slide 36: Address Subdivision
Figure: For this cache, the lower portion of the address is used to select a cache entry consisting of a data word and a tag.
This cache holds 1024 words or 4 KiB.
Notes: This cache holds 1024 words or 4 KiB. We assume 32-bit addresses in this chapter. The tag from the cache is compared against the upper portion of the address to determine whether the entry in the cache corresponds to the requested address. Because the cache has 210 (or 1024) words and a block size of one word, 10 bits are used to index the cache, leaving 32 −10 − 2 = 20 bits to be compared against the tag. If the tag and upper 20 bits of the address are equal and the valid bit is on, then the request hits in the cache, and the word is supplied to the processor. Otherwise, a miss occurs.

## Slide 37: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
Self Study
Notes: Note: In book 16 is written as 6, correct that in your book.

## Slide 38: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 39: Miss Rate versus Block Size
FIGURE #: Miss rate versus block size. Note that the miss rate actually goes up if the block size is too large relative to the cache size. Each line represents a cache of different size. (This figure is independent of associativity, discussed soon.) This data is based on SPEC92.
Cache sizes

## Slide 40: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 41: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But this approach makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full
Notes: Effective CPI = [100 + (10 * 100)]/100 = 11

## Slide 42: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 43: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%
Self Study
Notes: Note: I-cache => Instruction cache
D-cache => Data cache

## Slide 44: Example: Intrinsity FastMATH
Figure: The 16 KiB caches in the Intrinsity FastMATH each contain 256 blocks with 16 words per block.
Self Study
Notes: The tag field is 18 bits wide and the index field is 8 bits wide, while a 4-bit field (bits 5–2) is used to index the block and select the word from the block using a 16-to-1 multiplexor. In practice, to eliminate the multiplexor, caches use a separate large RAM for the data and a smaller RAM for the tags, with the block offset supplying the extra address bits for the large data RAM. In this case, the large RAM is 32 bits wide and must have 16 times as many words as blocks in the cache.

## Slide 45: 5.4 Measuring and Improving Cache Performance

## Slide 46: Measuring Cache Performance
§5.4 Measuring and Improving Cache Performance

## Slide 47: Measuring Cache Performance
With simplifying assumptions:
§5.4 Measuring and Improving Cache Performance

## Slide 48: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPI is 5.44/2 =2.72 times faster
Notes: I-cache: instruction cache
D-cache: data cache

## Slide 49: Average Access Time
Hit time is also important for performance
Average Memory Access Time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 50: Performance Summary
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 51: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 52: Associative Cache Example
Notes: 12 = 1100b => so lower 3 digit =100b (or, 4).

## Slide 53: Spectrum of Associativity
For a cache with 8 entries

## Slide 54: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
  Block access sequence mod 4
    [0 mod 4 = 0] , [8 mod 4 = 0], [6 mod 4 = 2]
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
Time

## Slide 55: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
Time
Time

## Slide 56: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 57: Set Associative Cache Organization
Figure: The implementation of a four-way set-associative cache requires four comparators and a 4-to-1 multiplexor.
Notes: The comparators determine which element of the selected set (if any) matches the tag. The output of the comparators is used to select the data from one of the four blocks of the indexed set, using a multiplexor with a decoded select signal. In some implementations, the Output enable signals on the data portions of the cache RAMs can be used to select the entry in the set that drives the output. The Output enable signal comes from the comparators, causing the element that matches to drive the data outputs. This organization eliminates the need for the multiplexor.

## Slide 58: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 59: Multilevel Caches
To close the gap further between the fast clock rates of modern processors and the increasingly long time required to access DRAMs, most microprocessors support an additional level of caching.
This second-level cache is normally on the same chip and is accessed whenever a miss occurs in the primary cache.
If the second-level cache contains the desired data, the miss penalty for the first-level cache will be essentially the access time of the second-level cache, which will be much less than the access time of main memory.
If neither the primary nor the secondary cache contains the data, a main memory access is required, and a larger miss penalty is incurred.

## Slide 60: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 61: Multilevel Cache Example
With just primary cache
  Miss penalty = = = 400 cycles
    Remember Giga => and nano =>
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 62: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 400 cycles (main memory access)
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 63: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 64: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 65: Interactions with Software
For large arrays, Radix Sort has an algorithmic advantage over Quicksort in terms of number of operations.
Quicksort consistently has many fewer misses per item to be sorted.
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access
Figure: Comparing Quicksort and Radix Sort by: (a) instructions executed per item sorted,
(b) time per item sorted, and
(c) cache misses per item sorted.
Self Study
Notes: This data is from a paper by LaMarca and Ladner [1996]. Due to such results, new versions of Radix Sort have been invented that take memory hierarchy into account, to regain its algorithmic advantages. The basic idea of cache optimizations is to use all the data in a block repeatedly before it is replaced on a miss

## Slide 66: Lesson
Lesson learnt from the previous slide:
The basic idea of cache optimizations is to use all the data in a block repeatedly before it is replaced on a miss.
=> For example, for the matrix multiplication:
Instead of operating an entire row or columns of an array, blocked algorithms operate on submatrices or blocks.

## Slide 67: Software Optimization via Blocking
Goal: maximize accesses to data before it is replaced
Consider inner loops of DGEMM:
for (int j = 0; j < n; ++j)
{
double cij = C[i+j*n];
for( int k = 0; k < n; k++ )
cij += A[i+k*n] * B[k+j*n];
C[i+j*n] = cij;
}

## Slide 68: DGEMM Access Pattern
C, A, and B arrays
older accesses
new accesses

## Slide 69: Cache Blocked DGEMM
1 #define BLOCKSIZE 32
2 void do_block (int n, int si, int sj, int sk, double *A, double
3 *B, double *C)
4 {
5 for (int i = si; i < si+BLOCKSIZE; ++i)
6 for (int j = sj; j < sj+BLOCKSIZE; ++j)
7 {
8 double cij = C[i+j*n];/* cij = C[i][j] */
9 for( int k = sk; k < sk+BLOCKSIZE; k++ )
10 cij += A[i+k*n] * B[k+j*n];/* cij+=A[i][k]*B[k][j] */
11 C[i+j*n] = cij;/* C[i][j] = cij */
12 }
13 }
14 void dgemm (int n, double* A, double* B, double* C)
15 {
16 for ( int sj = 0; sj < n; sj += BLOCKSIZE )
17 for ( int si = 0; si < n; si += BLOCKSIZE )
18 for ( int sk = 0; sk < n; sk += BLOCKSIZE )
19 do_block(n, si, sj, sk, A, B, C);
20 }
Self Study

## Slide 70: Blocked DGEMM Access Pattern
Unoptimized
Blocked
Self Study

## Slide 71: Dependability
Fault: failure of a component
  May or may not lead to system failure
Redundancy  Reliability
or, Dependability
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
§5.5 Dependable Memory Hierarchy

## Slide 72: Dependability Measures
Reliability measure: mean time to failure (MTTF)
: Annual Failure Rate (AFR)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair. If MTTR  0, Availability  1.0.
Self Study

## Slide 73: Error Correcting/Detecting Code
The Hamming Single Error Correcting Code (SEC)
&
Double Error Detecting Code (DEC)

## Slide 74: Hamming Code
Richard Hamming
  Turing Award in 1968
Linear error-correcting code
  Single Error Correcting Double Error Detecting (SECDED) variant is widely used in RAM and some secondary storage
Adding additional bits to detect and correct errors
  Increasing redundancy

## Slide 75: Hamming Code
Bit positions that are powers of two are used as parity bits
  That is, bit positions 1, 2, 4, 8, 16, 32, … are parity bits
The real data resides in remaining bits
  That is, bit positions 3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, …
Overhead is large at first, then tails off:
  For 1 bit of real data, a 3-bit hamming code would be needed (123)
  For 2 bits of real data, a 5-bit hamming code is needed (12345)
  For 4 bits of real data, a 7-bit hamming code is needed (1234567)

## Slide 76: Hamming Code

## Slide 77: Hamming Code Example
Ex: You want to store the 8-bit string 10011010
  You need a 12-bit hamming code to store 8-bits of data:
  ??1?001?1010
  p1p21p3001p41010
For p1 check bits: 1 3 5 7 9 11
  P1-1-0-1-1-1-
    We have even number of 1s (4). Therefore, p1 = 0 (0 for even, 1 for odd)
0p21p3001p41010
For p2 check bits: 2 3 6 7 10 11
  -P21--01--01-
    Odd number of 1s (3). P2 = 1
011p3001p41010

## Slide 78: Hamming Code Example
For p3 check bits: 4 5 6 7 12
  ---P3001----0
    Odd number of 1s (1). Therefore, p3 = 1
0111001p41010
For p4 check bits: 8 9 10 11 12
  -------P41010
    Even number of 1s (2). P4 = 0
011100101010

## Slide 79: Hamming Code Example
Assume that you have a bit sequence 011100101110
Step 1: Check sequence for Parity bit 1
  0-1-0-1-1-1-
    Even number of 1s. NO PROBLEM
Step 2: Check sequence for Parity bit 2
  -11- -01- -11-
  Odd number of 1s. ERROR

## Slide 80: Hamming Code Example
Step 3: Check sequence for Parity bit 3
  - - -1001- - - -0
  Even number of 1s. NO PROBLEM
Step 4: Check sequence for Parity bit 4
  - - - - - - - 01110
  Odd number of 1s. ERROR
Error in Parity bit 2 (Second bit) and parity bit 4 (Eighth bit)
  2 + 8 = 10th bit is wrong
  Invert the 10th bit!
Error sequence 011100101110
Correct sequence 011100101010

## Slide 81: Hamming Code Example
Brainstorm
  2 + 8 = 10th bit is wrong! HOW?
P1 : 1 3 5 7 9 11
P2 : 2 3 6 7 10 11
P3 : 4 5 6 7 12
P4 : 8 9 10 11 12
  Error in P2 and P4, No error in P1 and P3.
  Error must occur in the intersection of P2 and P4.
  Also, it cannot be in other parity bit sequence.
    If it is, that sequence would be wrong as well.
  Intersection of P2 and P4 => 10 11
  11 is in p1 sequence so it is correct since p1 is correct.
  Error in bit 10

## Slide 82: Hamming Code Example
How about 2 bit error?
  Correct Number 011100101010
  2-bit error 011100001110
P1 => 0-1-0-0-1-1- Error
P2 => -11- -00- -11- No Error
P3 => - - -1000- - - -0 Error
P4 => - - - - - - - - 01110 Error
Not possible to find which bits are not correct.
We use one more parity bit at the end of the number to check all 1s in the number.
E.g. 011100101010 => 0111001010100
  Even number of 1s. Last parity bit value = 0

## Slide 83: RAID Level 2 – Hamming Code
Thinking Machines CM-2 used RAID Level 2 with 32-bit words and adding 6 ECC bits to form a 38-bit Hamming word
  An extra bit for word parity was added as well
  This machine used 39 drives, storing one bit on each drive
  The Good:
    Throughput: 32 sectors of data read in a single sector read time
    With the ECC, drive failures can be handled on the fly
  The Bad:
    Nearly 1/5 overhead (you need 39 bits for a 32-bit data word)
    RAID Controller must do a Hamming checksum for every word
  The Ugly:
    All 39 drives must be synchronized
  RAID 2 is outdated since disks now employ ECC in the controller
Self Study

## Slide 84: RAID Level 2 – Hamming Code
Data is striped at word level, instead of sector level. A single bit is stored on each disk.
Remaining (non-data) disks are used to store a Hamming code: 4 data bits, 3 HC bits.
Drives must be synchronized in terms of arm position and rotational position.
A bad sector on one of the drives renders this sector useless for the drive set.
Self Study
Notes: ECC -> Error correcting code

## Slide 85: 5.6 Virtual Machines: Virtualization
Multi-processors/computers attempt to make many machines an integrated resource (one computer with the power of 20)
  Virtualization attempts the opposite: make a single machine appear as multiple independent systems
  Viewed another way though, virtualization is similar
    Instead of using multiple physical machines in a multicomputer or multiprocessor, we create multiple virtual machines
  Consider a company with many servers (web, email, ftp, etc.)
    These services may be hosted on separate machines
    If the web server crashes, email and ftp are unaffected
      Usually such crashes are caused by software failure
      A virtual machine could be used to run all servers on 1 system but still maintain the fault tolerance of having separate servers
Self Study

## Slide 86: Virtualization
Virtualization: Virtualization refers to technologies designed to offer a layer of abstraction between computer hardware systems and the software running on them. It can be a virtual version of computer hardware platform, operating system, a server, I/O systems, a storage device or network resources.
Advantages of Virtualization*:
  Allow running multiple OS and applications on a single computer.
  Combine H/W to obtain higher productivity from fewer servers and reduce hardware cost.
  Ease the manageability significantly and allow monitoring and deploying new application conveniently.
  *See: http://www.vmware.com/virtualization/
Self Study
Notes: http://.www.vmware.com/virtualization/virtualization-basics/what-is-virtualization.html
H/W => Hardware
See http://bcove.me/x9zhalcl
See http://bcove.me/ihjiwkd1

## Slide 87: Virtualization
Figure (a) Hypervisor (VMWare/ESX product here) allows running several Virtual Machines (VMs) on top of it. (b) Each VM can run guest OS, OS allows running applications (apps).
(a)
(b)
Bare Metal/Server
Hypervisor (type 1) creates a layer of OS independence
Operating System
Self Study
Notes: See www.vmware.com
ESX stands for Elastic Sky X
ESXi => ESX + integrated [that is ‘i’ is for ‘integrated’]

## Slide 88: Virtualization
If a standalone OS crashes, the entire system needs rebooting
With virtualization, a hypervisor runs in kernel mode
  The hypervisor is far less complex than an entire OS (less buggy)
OSes run on top of the hypervisor
  If an OS crashes, it can be restarted by the hypervisor
  It does not bring the entire machine down, only the given OS
  In fact, a hypervisor could run multiple instantiations of the same OS (say Windows)
    One copy runs the email server, another the web server
    If one BSoDs (Blue Screen of Death), then the others are unaffected
    This isolation allows the fault tolerance of multiple machines without the associated cost
  Unless the hardware fails!
Self Study

## Slide 89: Virtualization
Some software is not designed to run multiple instantiations
  The software may keep specific configuration files
  Instead of buying a new machine for each instantiation of the software that is needed, virtualization can be used
Virtualization also simplifies checkpointing and migration
  We can migrate an entire OS image to another machine
    It’s all stored in memory by the hypervisor
  If we run an OS on bare hardware, migrating processes is difficult because necessary info is in the OS system tables
  But with virtualization, we move the entire OS running the app
Self Study

## Slide 90: Virtualization
Virtual machines can be used to run legacy code
  Instead of keeping a dedicated machine that runs Win95
Virtual machines can also be used for software development
  Portability is a big concern for software developers
  The code should be tested on as many OSes as possible
    Instead of buying a separate machine for each OS
      Many virtual machines run the different OSes for testing
Self Study

## Slide 91
Figure: (a) A type 1 hypervisor. (b) A type 2 hypervisor.
Type 1 vs 2 Hypervisors
Tanenbaum, Modern Operating Systems 3 e, (c) 2008 Prentice-Hall, Inc. All rights reserved. 0-13-6006639
Hardware
Hardware
(a)
(b)
Self Study

## Slide 92
Type 1 vs 2 Hypervisor
Tanenbaum, Modern Operating Systems 3 e, (c) 2008 Prentice-Hall, Inc. All rights reserved. 0-13-6006639
Type 1 hypervisor software:
  VMware ESX/ESXi
  Hyper-V (from Microsoft)
  XenServer (from Citrix)
  Oracle VM Server for SPARC
  Oracle VM Server for x86
  IBM's z/VM
Type 2 hypervisor software:
  VMware Workstation
  Fusion (for Mac OS host)
  VirtualBox
Self Study

## Slide 93: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault
§5.7 Virtual Memory
Self Study

## Slide 94: Address Translation
Fixed-size pages (e.g., 4K)
Self Study

## Slide 95: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms
Self Study

## Slide 96: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk
Self Study

## Slide 97: Translation Using a Page Table
Self Study

## Slide 98: Mapping Pages to Storage
Self Study

## Slide 99: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written
Self Study
Notes: aka => also known as

## Slide 100: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software
Self Study

## Slide 101: Fast Translation Using a TLB
Self Study

## Slide 102: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction
Self Study

## Slide 103: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not preset
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur
Self Study

## Slide 104: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction
Self Study

## Slide 105: TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address
Figure: The TLB and cache implement, the process of going from a virtual address to a data item in the Intrinsity FastMATH.
Self Study
Notes: This figure shows the organization of the TLB and the data cache, assuming a 4 KiB page size. This diagram focuses on a read. Note that the tag and data RAMs are split. By addressing the long but narrow data RAM with the cache index concatenated with the block offset, we select the desired word in the block without a 16:1 multiplexor.
While the cache is direct mapped, the TLB is fully associative: Implementing a fully associative TLB requires that every TLB tag be compared against the virtual page number, since the entry of interest can be anywhere in the TLB. If the valid bit of the matching entry is on, the access is a TLB hit, and bits from the physical page number together with bits from the page offset form the index that is used to access the cache.

## Slide 106: Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (aka kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode
  System call exception (e.g., syscall in MIPS)
Self Study

## Slide 107: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
§5.8 A Common Framework for Memory Hierarchies
The BIG Picture

## Slide 108: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 109: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 110: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 111: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 112: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size
Self Study

## Slide 113: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.

## Slide 114: Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1

## Slide 115: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; sufficient time elapses, P2 reads X  read the value written by P1 (called Write- Propagation)
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X observed by all processors (called Write-Serialization)
Self Study

## Slide 116: Cache Coherence Protocols
Snooping protocols
  Each cache monitors bus reads/writes; so if necessary, each corresponding processor can update the status/value of the shared variable/block.
  Can be implemented for UMA processors
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory; directory basically keeps track of the sharing status of a block of memory
  Suitable for NUMA processors
    Non-uniform memory access

## Slide 117: Cache Write Protocols
Write-Invalidate
  A process obtains exclusive access of a variable/block before writing into it by invalidating all other copies of it.
Write-update
  A process updates all the other shared copies of the variable/block when a process writes into it.

## Slide 118: Snooping with Write-invalidate
Computer starts, cache empty, block X is in main memory
PA (CPUA) wants to read X, PA checks PA’s cache, no copy exists, so places a ‘read X’ request on the bus, and everyone see the request.
It is expected that if X exists in other processors’ cache they should supply X to PA (Why?*) Here, no processor has X in cache, so main memory supplies X to PA though the bus.
  *Why: it is faster to transfer value from cache than from main memory.
PA places X in its cache with status shared ‘S’, indicating it is sharable and for read purpose.
Now, say, PB wants to read X; PB will check its cache, it is not there, so it will place a request on the bus.
All the processors will see the request but only PA can and will supply X to PB.
CPUA
Memory
Cache
CPUB
Cache
CPUC
Cache
CPUD
Cache
Bus: all processors snoop on the bus
Notes: *Why: it is faster to transfer value from cache than from main memory.

## Slide 119: Snooping with Write-invalidate
PB now places X in its cache with status shared ‘S’, indicating it is sharable and for reading.
Now, PC wants to write X, cache empty, so places ‘write X’ on bus.
PA and PB, don’t supply X while in ‘S’ state in response to write request (Why?), main-memory supplies it to PC. PC stores X in cache with modified ‘M’ status.
(Ans:) PA and PB, invalidates (‘I’) their cache copies of X. PC can now modify X as many time as it needs without broadcasting about it and will write-back to main-memory when it needs to evict X from the cache of PC.
CPUA
Memory
Cache X
CPUB
Cache X
CPUC
Cache
CPUD
Cache
Bus: all processors snoop on the bus
X
S
S

## Slide 120: Snooping with Write-invalidate
Now PB wants to read X. PC supplies the value to PB. PB places X in its own cache and marks ‘S’. PC marks its X in cache from ‘M’ to ‘S’. Since, it is a transition from ‘M’ to ‘S’, PC must update (write-back) X in main-memory.
Now, if either B or C wants to write, it will place ‘Write X’ on the bus and it will change its cache X’s status from ‘S’ to ‘M’ and other processors, if has a copy will mark from ‘S’ to ‘I’.
Here, based on bus information (by snooping on bus) processors update their cache at their own responsibility.
‘Write-propagation’ (check slide#115) is satisfied in the above steps.
CPUA
Memory
Cache X
CPUB
Cache X
CPUC
Cache X
CPUD
Cache
Bus: all processors snoop on the bus
X
I
I
M

## Slide 121: Snooping with Write-invalidate
Now, the ‘Write-Serialization’ (check slide#115) is satisfied because of the bus properties. Assume, processor B and C both wants to write X, say values 10 and 15 respectively at the same time.
Bus arbitration will allow one to speak in the bus, hence write-serialization will be maintained – it may be B then C or, C then B, however, all other processor will see the same order or get the same final value.
For example, if processor A will read X=15 (when B writes and then C writes) then, D will read the same that is X=15, but not X=10, – otherwise, the ‘write-serialization’ is not maintained.
CPUA
Memory
Cache X
CPUB
Cache X
CPUC
Cache X
CPUD
Cache
Bus: all processors snoop on the bus
X
I
S
S

## Slide 122: Directory Based Protocols
Problem: Snoopy based protocol has scaling problem; as the number of node increases the bus becomes too busy to function.
Solution: Directory based solution.
In Directory based solution:
  there is no bus but scalable network such as mesh. So, no need to broad-cast all messages all the time, rather point-to-point communication is possible.
  No central memory, rather it is distributed among the nodes. E.g.: in the system there are 256 nodes and each has 16MB, then total memory of the system is 256 x 16MB = 4GB.
  The memory is statically allocated among the nodes as: 0-16M in node #0, 16M-32M in #1, ..
So, for example, if Node#0 (N0) or, Processor #A (PA) is looking for block X, at memory location 35th M, then it needs to contact node#2 if the entry is not in node#0’s own cache. Since node#2 has 32M-48M memory.
/ ProcessorA
/ PB
Self Study

## Slide 123: Directory Based Protocols
Assume, X is not in N0’s own cache. N0 forwards a ‘read X’ request to N2.
Note, the request is point-to-point unlike the bus based snooping protocol, so less or no traffic problem to other processors.
N2’s directory keeps track of its memory block X, marks it shareable / shared ‘S’ with a empty list (‘list’ is about who is having a copy of it).
Now, N0 reads N2’s memory for X and N2’s directory at the same time for status, finds it is ‘S’, implies a clean copy (not modified: ‘M’ or, not Invalidated: ‘I’) to be used.
N0 gets the copy of X and put it in its own cache with status ‘S’ (shared / for reading only) and places ‘0’ in the list in N2’s directory as: ‘S:0’
Self Study

## Slide 124: Directory Based Protocols
Now, N1 needs to read X. It could not find X in its own cache so sends a request to N2 and gets a copy and places it in N1’s own cache. This is updated in N2’s directory list as from ‘S:0’ to ‘S:0,1’.
Now say, N255 wants to ‘Write X’.
Self Study

## Slide 125: Directory Based Protocols
Say N255 does not find it in its cache, thus it sends ‘Write X’ request to N2. The X for N255 needs to be an exclusive copy for writing.
So, directory of N2 sends command to N0 and N1 to invalidate their cache copies of X and proceeds after receiving ‘ACK’ (acknowledge) from them – because the architecture is NUMA and no snooping available – so it must be confirmed.
After getting ACKs, N2’s directory sends copy of X to N255. N255 caches X in it with mark ‘M’ and directory of N2 updates the list as: ‘M:255’ for block X.
Self Study

## Slide 126: Directory Based Protocols
Now, N0 wants to read X, finds invalidated cache, so sends request to N2.
N2 finds from its directory that N255 is modifying it. So, N2 sends request to N255 to supply update copy of X. N255 downgrades its cache for X from M to S (MS, subject to update the original source (memory) in N2.), so getting the copy of X from N255, N2 updates its memory for X. N2’s directory then sends X to N0. N2 updates its directory from ‘M:255’ to ‘S:0, 255’. N0 caches the copy of X and set status to ‘S’.
If N0, instead of a read X, would ask for a write X, then N255 would have invalidated (‘I’) its cache rather making it ‘S’. And, N0 receiving updated X, would have cashed it with status ‘M’.
Self Study

## Slide 127: Synchronization in Shared Memory Programs (Act of Lock)
Self Study

## Slide 128: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization
Recall, Ch2
Self Study

## Slide 129: Test and Set Lock (TSL)
TSL REGISTER, LOCK (hardware support)
    Reads the contents of the memory word lock into register RX and stores a non-zero value at the memory address lock.
    The memory bus is locked during this operation so no other process or CPU can access memory (e.g. change Lock’s value)
Mutual Exclusion
  enter_region:
  TSL REGISTER, LOCK | copy Lock to Reg and set Lock to 1
  CMP REGISTER, #0 | was the Lock zero?
  JNE enter_region | if Lock was nonzero, jump to top of loop
  RET | return to caller, critical region entered
  leave_region:
MOVE LOCK, #0 | store 0 in Lock
RET | return to caller
Recall, Ch2
Self Study

## Slide 130: Synchronization in Shared Memory Programs
Initially, Lock variable L=0 in memory
PA runs: TSL; sets L=1 successfully, PA cache L=1, with status: M
PA enters CS (Critical Section) and now PB wants to get in CS
PB runs: TSL; L in PA is invalidated, Mem: L=1; cached in PB runs with L=1, status: M; so can not get in CS but loops.
Now PC wants to get in CS: invalidates the entry in PB and will have a copy of L=1 in PC’s cache.
Once PA releases (setting L=0); M in PA’s cache. Others are in loop. Now, M S makes memory L=0.
Assume, PC’s TSL call is ahead of PB’s. So, PC will acquire the lock, …
CPUA
Memory
Cache
CPUB
Cache
CPUC
Cache
CPUD
Cache
Bus: all processors snoop on the bus
L=0
Self Study

## Slide 131: Synchronization in Shared Memory Programs
There is no violation of the purpose of the lock but it will be extremely inefficient keeping the common bus busy as the lock variable will be heavily moving among nodes’ caches and it happened when PA was in CS.
To reduce the bus traffic we can simply use Test(L) to read L in a loop (so the read will be only from local cache) and once L=0, then we can run TSL(L) which involves ‘write’. So the modified code could be:
CPUA
Memory
Cache
CPUB
Cache
CPUC
Cache L=1, M.
CPUD
Cache
Bus: all processors snoop on the bus
L=1
Self Study

## Slide 132: Synchronization in Shared Memory Programs
In higher-level language:
Before:
  While (TSL(L)); // read only
  //from local cache
After
  Repeat
    While (L); // loop when L=1
  Until (!(TSL(L));
In assembly code
After:
enter_region:
Test REGISTER, L; L is LOCK
CMP REGISTER, #0
JNE enter_region
TSL REGISTER, L;
CMP REGISTER, #0
JNE enter_region
RET
Basically, in assembly, the Test is having the value of lock in Register to test whether it is ‘0’ of ‘1’ . And, register is local, and so no write involves the global L.
Self Study

## Slide 133: Multilevel On-Chip Caches
§5.13 The ARM Cortex-A8 and Intel Core i7 Memory Hierarchies
Self Study

## Slide 134: 2-Level TLB Organization
Self Study

## Slide 135: Pitfalls
Byte vs. word addressing
  Example: 32-byte direct-mapped cache, 4-byte blocks
    Byte 36 maps to block 1
    Word 36 maps to block 4
Ignoring memory system effects when writing or generating code
  Example: iterating over rows vs. columns of arrays
  Large strides result in poor locality
§5.15 Fallacies and Pitfalls
Self Study

## Slide 136: Pitfalls
In multiprocessor with shared L2 or L3 cache
  Less associativity than cores results in conflict misses
  More cores  need to increase associativity
Using AMAT to evaluate performance of out-of-order processors
  Ignores effect of non-blocked accesses
  Instead, evaluate performance by simulation
Self Study

## Slide 137: Pitfalls
Extending address range using segments
  E.g., Intel 80286
  But a segment is not always big enough
  Makes address arithmetic complicated
Implementing a VMM on an ISA not designed for virtualization
  E.g., non-privileged instructions accessing hardware resources
  Either extend ISA, or require guest OS not to use problematic instructions
Self Study

## Slide 138: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors
§5.16 Concluding Remarks