## Slide 1: Chapter 6
Parallel Processors from Client to Cloud
Abdullah Yasin Nur

## Slide 2: Introduction
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability
    E.g. Hadoop for processing big-data. Hadoop platform is designed to solve problems where you have a lot of data. Hadoop is designed to run on a large number of machines that don’t share any memory or disks.
  Availability / Reliability
    If a single processor fails in a multiprocessor with n processor, these system would continue to provide service with n-1 processors.
  Power Efficiency
    One big processor vs many smaller processors
§6.1 Introduction

## Slide 3: Introduction
Task-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing of a program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)
Cluster
  A set of computers connected over a local area network that function as a single large multiprocessor. Basically, it is composed of microprocessor housed in many independent server.
§6.1 Introduction

## Slide 4: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., quad-core Xeon e5345 or Core i7
Software
  Sequential: e.g., matrix multiplication
    Sequential programming involves a consecutive and ordered execution of processes one after another
  Concurrent: e.g., operating system
    A concurrent system is one where a computation can advance without waiting for all other computations to complete.

## Slide 5: Hardware and Software
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 6: Parallel Programming
Parallel software is the bottleneck.
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs

## Slide 7: Parallel Programming
Sequential part can limit speedup
Remember the analogy in Chapter 1:
  Eight reporters trying to write a single story in hopes of doing the work eight times faster.
  To succeed, the task must be broken into eight equal-sized pieces, because otherwise some reporters would be idle while waiting for the ones with larger pieces to finish.
  Another speed-up obstacle could be that the reporters would spend too much time communicating with each other instead of writing their pieces of the story.

## Slide 8: Amdahl’s Law
Question: Suppose we want to achieve a speed-up of 90 times faster with 100 processors. What percentage of the original computation can be sequential?

## Slide 9: Amdahl’s Law

## Slide 10: Amdahl’s Law
– Execution time affected

## Slide 11: Amdahl’s Law
Assume that execution time before = 1
= 0.999
Need sequential part to be 0.1% of original time
= 100
because of 100 processors

## Slide 12: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10
Assumes load can be balanced across processors

## Slide 13: Scaling Example (cont)
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91
Assuming load balanced

## Slide 14: Instruction and Data Streams
One categorization of parallel hardware proposed in the 1960s is still used today.
  Based on the number of instruction streams and the number of data streams
SISD : Single instruction stream, single data stream.
  A uniprocessor
MIMD : Multiple instruction stream, Multiple data stream.
  A multiprocessor
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 15: Instruction and Data Streams
SPMD : Single Program, Multiple Data streams
  The conational MIMD programming model, where a single program runs across all processors
SIMD : Single Instruction stream, Multiple Data streams
  The same instruction is applied to many data streams, as in a vector processor.
 |  | Data Streams | 
 |  | Single | Multiple
Instruction Streams | Single | SISD: Intel Pentium 4 | SIMD: SSE instructions of x86
 | Multiple | MISD: No examples today | MIMD: Intel Core i7
§6.3 SISD, MIMD, SIMD, SPMD, and Vector

## Slide 16: Comparing Vector to Conventional Code
Suppose, we extend the MIPS instruction set architecture with vector instructions and vector registers.
Also, vector operations use the same name as MIPS operation, but with letter “V” appended.
  addv.d: adds two double-precision vectors
  addvs.d: adds a scalar register to each elements of a vector register
  lv, sv: vector load and vector store an entire vector of double-precision
Now we will see the conventional MIPS code vs the vector MIPS code for:
Y = a × X + Y
where, X and Y are vectors of 64 double-precision floating-point numbers, initially resident in memory, and a is a scalar double-precision variable (so called DAXPY example).
Assume, starting address of X and Y are $s0 and $s1, respectively.
Self Study
Notes: DAXPY stands for double precision a × X plus Y.
AVX => Advanced Vector Extension => 32 vector registers, each has 64 64 bit elements.

## Slide 17: Example: DAXPY (Y = a × X + Y)
Conventional MIPS code
l.d $f0,a($sp) ;load scalar a addiu $t0,$s0,#512 ;upper bound of what to load loop: l.d $f2,0($s0) ;load x(i) mul.d $f2,$f2,$f0 ;a × x(i) l.d $f4,0($s1) ;load y(i) add.d $f4,$f4,$f2 ;a × x(i) + y(i) s.d $f4,0($s1) ;store into y(i) addiu $s0,$s0,#8 ;increment index to x addiu $s1,$s1,#8 ;increment index to y subu $t0,$t0,$s0 ;compute bound bne $t0,$zero,loop ;check if done
Vector MIPS code
l.d $f0,a($sp) ;load scalar a lv $v1,0($s0) ;load vector x mulvs.d $v2,$v1,$f0 ;vector-scalar multiply lv $v3,0($s1) ;load vector y addv.d $v4,$v2,$v3 ;add y to product sv $v4,0($s1) ;store the result
Self Study
Notes: Double is 8 bytes number, so, 8 x 64 = 512 (the upper bound).

## Slide 18: Comparing Vector to Conventional Code
In that example, vector processor greatly reduces the dynamic instruction bandwidth: 6 instructions vs 600 instructions, specifically.
The reduction in its fetch and execution saves energy.
In conv. MIPS, every add .d must wait for a mul .d, every s.d must wait for the add.d and every add.d & mul.d must wait for l.d.
On Vec. Proc., every vector ins. will only stall for the first element in the vector, rest will have smooth flow.
Self Study

## Slide 19: Vector Processors
Highly pipelined function units
Stream data from/to vector registers to units
  Data collected from memory into registers
  Results stored from registers to memory
Example: Vector extension to MIPS
  32 × 64-element registers (64-bit elements)
  Vector instructions
    lv, sv: load/store vector
    addv.d: add vectors of double
    addvs.d: add scalar to each element of vector of double
Significantly reduces instruction-fetch bandwidth
Self Study

## Slide 20: Vector vs. Scalar
Vec. is equivalent to execute an entire loop
Each element in vector is independent, so hardware does not have to check for data-hazards within a vector instruction.
Vec. architecture and compilers are well known of making efficient usage of MIMD for data-level parallelism
H/W need to check for data-hazard betn 2 vector ins once per vector operand, not for every elements. Saves energy.
Self Study

## Slide 21: Vector vs. Scalar
For Vec., fetching is mostly from aligned memory element, thus latency is seen once for vector but not for each elements.
As an entire loop is replaced by a vector ins, control hazards are non-existent.
Savings in ins bandwidth, hazard checking and efficient use of memory help save energy.
Thus, replacing scalar operations with vector operations as much as possible is a better choice.
Self Study
Notes: Ins => instruction

## Slide 22: Vector vs. Multimedia Extensions
Vector instructions have a variable vector width, multimedia extensions have a fixed width
Vector instructions support strided access, multimedia extensions do not
Vector units can be combination of pipelined and arrayed functional units:
Self Study

## Slide 23: Hardware Multithreading
§6.4 Hardware Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle => Interleaved execution of multiple threads, round-robin style
  If one thread stalls – it is skipped but others are executed => can hide throughput losses due to stall
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)

## Slide 24: Simultaneous Multithreading (SMT)
SMT uses the resources (Functional Units) of a multiple-issue dynamically scheduled processor
  Exploits thread-level parallelism as well as ins. level parallelism (ILP)
  Within threads, dependencies handled by scheduling and register renaming conveniently
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches
Notes: FUs=> Functional Units

## Slide 25: Multithreading Example
Figure: How do 4 threads use the issue slots of a superscalar processor in different approaches?

## Slide 26: Multicore & other Shared Memory Multiprocessor
§6.5 Multicore and Other Shared Memory Multiprocessors
Question: given the difficulty of rewriting old programs to run well on parallel Hardware, what can computer designer do to simplify the task?
Ans:
  Provide a single physical address space that all processor can share. Ease the concern of the data location per processors, instead merely programs may be executed in parallel.
  This also makes all variables of a program available to any time to any processor.
  A shared memory multiprocessor (SMP) offers a single physical address space across all processors – which is also the case for multicore chips.
Notes: H/W => Hardware
S/W => Software

## Slide 27: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform memory access ) vs. NUMA (nonuniform ~)

## Slide 28: Example: Sum Reduction
Sum 64,000 numbers on 64 processor uniform memory access
  Each processor has ID: 0 ≤ Pn ≤ 63
  Partition 1000 numbers per processor
  Initial summation on each processor
sum[Pn] = 0;
for (i = 1000*Pn; i < 1000*(Pn+1); i = i + 1)
sum[Pn] = sum[Pn] + A[i];
Now need to add these partial sums
  Reduction: divide and conquer
  Half the processors add pairs, then quarter, …
  Need to synchronize between reduction steps

## Slide 29: Example: Sum Reduction
half = 64;
repeat
synch();
if (half%2 != 0 && Pn == 0)
sum[0] = sum[0] + sum[half-1];
/* Conditional sum needed when half is odd;
Processor0 gets missing element */
half = half/2; /* dividing line on who sums */
if (Pn < half) sum[Pn] = sum[Pn] + sum[Pn+half];
until (half == 1);
Self Study

## Slide 30: History of GPUs
Early video cards
  Frame buffer memory with address generation for video output
3D graphics processing
  Originally high-end computers
  Moore’s Law  lower cost, higher density
  3D graphics cards for PCs and game consoles
Graphics Processing Units
  Processors oriented to 3D graphics tasks
  Vertex/pixel processing, shading, texture mapping, rasterization
§6.6 Introduction to Graphics Processing Units

## Slide 31: GPU vs CPU
GPU are accelerators that supplement CPU for graphics works. GPU can not do all, so CPU completes it.
GPU’s problem sizes are few hundred MB to GB, but not hundreds of GB to TB.
GPU do not rely on multilevel cache, rather on hardware multithreading, as GPU executes hundreds to thousands of independent threads.
DRAM chips for GPUs are wider and are of higher bandwidth than DRAM of CPUs.
For GP-GPU, consider the transfer time from CPU to GPU, as GPU is rather a coprocessor.
Notes: GP-GPU: general purpose GPU

## Slide 32: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  NVIDIA’s CUDA (Compute Unified Device Architecture)

## Slide 33: NVIDIA GPU Architectures
GPU has 16 SIMD Lanes; i.e., GPU is a MIMD composed of multithreaded SIMD.
The SIMD instructions of these threads are 32 wide.
Figure: Block-diagram of the datapath of a multithreaded SIMD Processor
Notes: SIMD : Single Instruction stream Multi Data streams

## Slide 34: NVIDIA GPU Architectures
Basically, the GPU hardware has two levels of hardware schedulers:
  The Thread Block Scheduler that assigns blocks of threads to multithreaded SIMD processors, and
  the SIMD Thread Scheduler with a SIMD processor, which schedules when SIMD threads should run.
Notes: SIMD : Single Instruction stream Multi Data streams

## Slide 35: GPU Memory Structures
GPU memory is shared by the vectorized loops. All threads of SIMD instructions within a thread block share Local Memory.
Self Study

## Slide 36: Putting GPUs into Perspective
Feature | Multicore with SIMD | GPU
SIMD processors | 4 to 8 | 8 to 16
SIMD lanes/processor | 2 to 4 | 8 to 16
Multithreading hardware support for SIMD threads | 2 to 4 | 16 to 32
Typical ratio of single precision to double-precision performance | 2:1 | 2:1
Largest cache size | 8 MB | 0.75 MB
Size of memory address | 64-bit | 64-bit
Size of main memory | 8 GB to 256 GB | 4 GB to 6 GB
Memory protection at level of page | Yes | Yes
Demand paging | Yes | No
Integrated scalar processor/SIMD processor | Yes | No
Cache coherent | Yes | No
Self Study

## Slide 37: Guide to GPU Terms
Self Study

## Slide 38: Multiprocessors
A shared-memory multiprocessor is a computer system where two or more CPUs share full access to the memory system
  Memory system is the means of communication between CPUs
  Functions much like a single processor system
All processors in a multiprocessor can access all of memory
  UMA (Uniform Memory Access) multiprocessors have the property that every memory word takes the same time to access
  NUMA (Non-UMA) multiprocessors do not provide this guarantee
    This is dependent on the interconnect in use and RAM organization

## Slide 39: Multiple Processor Systems
Figure: (a) A shared-memory multiprocessor. (b) A message-passing multicomputer. (c) A wide area distributed system.

## Slide 40: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters, WSC, and Other Message-Passing MPs

## Slide 41: UMA Multiprocessors
Bus contention becomes the largest issue
  When a CPU wants to access memory it checks the bus
  If the bus is busy it must wait, otherwise it accesses memory
  This is fine for very few processors
    A 32 processor machine wouldn’t work well though
    The solution is to interpose a cache for each CPU
      But this creates its own set of problems
CPU
CPU
CPU
CPU
Memory
Bus-Based Architecture (without caching)
Shared
memory
Self Study

## Slide 42: UMA Multiprocessors
When a CPU wants to access memory it checks its cache
  Each cache block is marked as “read-only” or “read-write”
  A read-only block can be present in multiple caches but a read-write block can only be present in one
  If a CPU attempts to write a word that is in one or more caches, the bus hardware informs all other caches of the write
    If the word is modified in a RW cache, then it is written back from there
CPU
Memory
Cache
CPU
Cache
CPU
Cache
CPU
Cache
With caching:
Self Study

## Slide 43: UMA Multiprocessors
To use this configuration (dedicated bus for private memory) optimally, steps are taken to reduce bus traffic, such as:
  Compiler can place all the program text, string, constants and other read-only data, stacks, and local variables in private memories.
  The shared memory can then only be used for writable shared variables.
CPU
Memory
Cache
CPU
Cache
CPU
Cache
CPU
Cache
With caching and private memory:
Shared
memory
Private memory
Self Study

## Slide 44: Crossbar Switch UMA
Memory is broken into N banks accessed independently
  Contention is greatly reduced so more CPUs can be supported than the bus-based architecture
  The size of the crossbar (number of join points) grows as N2
    This is too expensive for really large installations
    But it provides good performance for moderate sized MPs
Self Study

## Slide 45: UMA Multiprocessors
Figure: (a) An 8 × 8 crossbar switch. (b) An open crosspoint. (c) A closed crosspoint.
Using Crossbar Switches:
Self Study

## Slide 46: NUMA Multiprocessors
UMA multiprocessors are limited in size
  A bus-based UMA can support only a handful of processors
    Bus contention becomes a problem quickly even with caching
  Crossbar switches are expensive which limits size as well
For large multiprocessor systems we must abandon UMA
  This means memory access times are variable
  Practically, it means non-local accesses will take a ‘long time’
    NUMAs still have a single address space visible to all CPUs
    Access to memory is still achieved via a load-store method
    But non-local accesses will likely to go over a network connection
      Can be far slower even than going to disk
Self Study

## Slide 47: NUMA Multiprocessors
Each processor is self contained with its own bus, RAM, etc.
  The interconnection network is used to connect the processors
  Access to local memory is ‘fast’, remote memory is ‘slow’
  Directory is used to keep track of caching across machines
Figure: A 256-node directory-based multiprocessor.
Self Study

## Slide 48: NUMA Multiprocessors
Why do we care that access times are not uniform?
  We don’t really care that accesses take ‘different’ times
    What we do care is that non-local accesses are very slow
    This forces the programmer of a NUMA architecture to be aware of the placement of data
      After all, if we access memory with no regard to local vs non-local, then the application may run slower on a NUMA than if we ran it on a single processor
    NUMA programmers must carefully place and process their data
      One way to alleviate some of the burden of accessing non-local data is to cache data from other processors
        But this opens up a whole new can of worms
Self Study

## Slide 49: Multicomputers
Multicomputers offer an alternative to shared memory MPs
  Multiprocessors with shared memory offer a simple communication model that programmers are familiar with
    This load-store approach allows for synchronization using locks, semaphores, monitors and other well-established techniques
    The problem is that multiprocessors are expensive to build
Multicomputers are tightly coupled CPUs with no shared memory
  They are easy and cheap to build using stripped commodity PCs
  Communication is done via message passing over the network
  High performance network cards and connectivity is used
  Message passing presents new challenges to the programmer

## Slide 50: Multicomputer Hardware
A node of a multicomputer consists of the CPU, memory, network interface card and occasionally a hard disk
  There is no need for other standard PC components such as a graphics card, monitor, keyboard, mouse, etc.
Interconnection Technology
  Each node has a NIC connected to one or two cables
    If one cable, it is connected to a switch
    If two cables, the node may be connected to other nodes directly
  There are a variety of connection topologies in use
    Each has its own purpose, strengths and weaknesses

## Slide 51: Multicomputer Systems
Figure: Hadoop Cluster
Notes: Ref: Intel

## Slide 52: Star Topology
Switch
Node
Node
Node
Node
Node
Node
Node
Node
Each node is connected to a central switch
  Modern switched Ethernets (suitable for small # of nodes)
  Diameter (longest path between any two nodes) is 2

## Slide 53: Ring Topology
Each node is connected to two adjacent nodes
  No switches are necessary (two cables out of each NIC)
  Diameter is n/2
Node
Node
Node
Node
Node
Node
Node
Node

## Slide 54: Grid Topology
Diameter is 2(√n -1) + 2 = 2√n
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Notes: n = number of nodes

## Slide 55: Double Torus Topology
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
Node
A grid with the edges circularly connected
  Reduces diameter further and improves fault tolerance

## Slide 56: Cube Topology
Diameter is 3 (corner to opposite corner)
Node
Node
Node
Node
Node
Node
Node
Node

## Slide 57: Hypercube Topology
A 4-dimensional hypercube is shown (n=16)
  Diameter scales with dimension of the hypercube (log2n)

## Slide 58: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models
Self Study

## Slide 59: Code or Applications?
Traditional benchmarks
  Fixed code and data sets
Parallel programming is evolving
  Should algorithms, programming languages, and tools be part of the system?
  Compare systems, provided they implement a given application
  E.g., Linpack, Berkeley Design Patterns
Would foster innovation in approaches to parallelism
Self Study

## Slide 60: Modeling Performance
Assume performance metric of interest is achievable GFLOPs/sec
  Measured using computational kernels from Berkeley Design Patterns
Arithmetic intensity of a kernel
  FLOPs per byte of memory accessed
For a given computer, determine
  Peak GFLOPS (from data sheet)
  Peak memory bytes/sec (using Stream benchmark)
Self Study

## Slide 61: Roofline Diagram
Attainable GPLOPs/sec
= Max ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )
Self Study

## Slide 62: Comparing Systems
Example: Opteron X2 vs. Opteron X4
  2-core vs. 4-core, 2× FP performance/core, 2.2GHz vs. 2.3GHz
  Same memory system
To get higher performance on X4 than X2
  Need high arithmetic intensity
  Or working set must fit in X4’s 2MB L-3 cache
Self Study

## Slide 63: Optimizing Performance
Optimize FP performance
  Balance adds & multiplies
  Improve superscalar ILP and use of SIMD instructions
Optimize memory usage
  Software prefetch
    Avoid load stalls
  Memory affinity
    Avoid non-local data accesses
Self Study

## Slide 64: Optimizing Performance
Choice of optimization depends on arithmetic intensity of code
Arithmetic intensity is not always fixed
  May scale with problem size
  Caching reduces memory accesses
    Increases arithmetic intensity
Self Study

## Slide 65: i7-960 vs. NVIDIA Tesla 280/480
§6.11 Real Stuff: Benchmarking and Rooflines i7 vs. Tesla
Self Study

## Slide 66: Rooflines
Self Study

## Slide 67: Benchmarks
Self Study

## Slide 68: Performance Summary
GPU (480) has 4.4 X the memory bandwidth
  Benefits memory bound kernels
GPU has 13.1 X the single precision throughout, 2.5 X the double precision throughput
  Benefits FP compute bound kernels
CPU cache prevents some kernels from becoming memory bound when they otherwise would on GPU
GPUs offer scatter-gather, which assists with kernels with strided data
Lack of synchronization and memory consistency support on GPU limits performance for some kernels
Self Study

## Slide 69: Multi-threading DGEMM
§6.12 Going Faster: Multiple Processors and Matrix Multiply
Use OpenMP:
void dgemm (int n, double* A, double* B, double* C)
{
#pragma omp parallel for
for ( int sj = 0; sj < n; sj += BLOCKSIZE )
for ( int si = 0; si < n; si += BLOCKSIZE )
for ( int sk = 0; sk < n; sk += BLOCKSIZE )
do_block(n, si, sj, sk, A, B, C);
}
Self Study

## Slide 70: Multithreaded DGEMM
Self Study

## Slide 71: Multithreaded DGEMM
Self Study

## Slide 72: Fallacies
Amdahl’s Law doesn’t apply to parallel computers
  Since we can achieve linear speedup
  But only on applications with weak scaling
Peak performance tracks observed performance
  Marketers like this approach!
  But compare Xeon with others in example
  Need to be aware of bottlenecks
§6.13 Fallacies and Pitfalls
Self Study

## Slide 73: Pitfalls
Not developing the software to take account of a multiprocessor architecture
  Example: using a single lock for a shared composite resource
    Serializes accesses, even if they could be done in parallel
    Use finer-granularity locking
Self Study

## Slide 74: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
SaaS (Software as a Service) importance is growing and clusters are a good match
Performance per dollar and performance per Joule drive both mobile and WSC (Warehouse Scale Computer) hardware, and parallelism is the key to delivering on those sets of goals.
§6.14 Concluding Remarks