## Slide 1: CSCI 3301: Computer Organization
Abdullah Yasin Nur

## Slide 2: Topic Coverage
Chapters
  Computer Abstraction and Technology
  Instructions: Language of the Computer
  Arithmetic for Computers
  The Processor
  Large and Fast: Exploiting Memory Hierarchy
  Parallel Processors from Client to Cloud

## Slide 3: Chapter 1
Computer Abstractions and Technology

## Slide 4: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive
§1.1 Introduction

## Slide 5: Classes of Computers
Personal computers
  General purpose, variety of software
  Subject to cost/performance tradeoff
Server computers
  Network based
  High capacity, performance, reliability
  Range from small servers to building sized

## Slide 6: Classes of Computers
Supercomputers
  High-end scientific and engineering calculations
  Highest capability but represent a small fraction of the overall computer market
Embedded computers
  Hidden as components of systems
  Stringent power/performance/cost constraints

## Slide 7: Supercomputers
America's latest supercomputer
Size of two tennis courts
Fastest supercomputer in the world
200,000 trillion calculations per second
"If every person on Earth completed one calculation per second, it would take the world population 305 days to do what Summit can do in 1 second“
Oak Ridge National Laboratory, Tennessee
https://www.ornl.gov/

## Slide 8: Classes of Computers
Personal computers
Server computers
Supercomputers
Embedded computers

## Slide 9: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google

## Slide 10: How do computers work?
Applications software
Systems software
Assembly Language
Machine Language
Architectural Issues
Sequential logic, finite state machines
Combinational logic, Arithmetic circuits
Boolean logic, 1s and 0s
Transistors
Semiconductors – Silicon used to build transistors
Properties of atoms, electrons and quantum dynamics

## Slide 11: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing

## Slide 12: Understanding Performance
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 13: Eight Great Ideas
Design for Moore’s Law
Use abstraction to simplify design
Make the common case fast
Performance via parallelism
Performance via pipelining
Performance via prediction
Hierarchy of memories
Dependability via redundancy
§1.2 Eight Great Ideas in Computer Architecture
Notes: Moore's law is the observation that the number of transistors in a dense integrated circuit doubles about every two years.

## Slide 14: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.3 Below Your Program
Notes: Application > Algorithm > System Software > OS > ISA > Microarchitecture > Register Transfer Level (RTL) > Gates > Circuits > Devices > Physics

## Slide 15: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 16: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.4 Under the Covers
The BIG Picture

## Slide 17: Touchscreen
PostPC device
Supersedes keyboard and mouse
Resistive and Capacitive types
  Most tablets, smart phones use capacitive
  Capacitive allows multiple touches simultaneously

## Slide 18: Opening the Box – Apple iPad 2 A1395
Capacitive multitouch LCD screen
3.8 V, 25 Watt-hour battery
Computer board

## Slide 19
19
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.8 The logic board of Apple iPad 2 in Figure 1.7. The photo highlights five integrated circuits. The large integrated circuit in the middle is the Apple A5 chip, which contains a dual ARM processor cores.
Apple 1GHz A5 dual-core Processor with a 200MHz bus and 512 MB of Samsung manufactured RAM.
Toshiba TH58NVG7D2FLA89 16GB NAND Flash.
Power management chip
Texas Instruments CD3240B0 11AZ4JT G1 touchscreen line driver.
S6T2MLC N33C50V Power Management IC.
(Refernce: iFixit, www.ifixit.com)
Notes: Logic printed circuit board:

## Slide 20
20
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.9 The processor integrated circuit inside the A5 package. The size of chip is 12.1 by 10.1 mm, and it was manufactured originally in a 45-nm process (see Section 1.5). It has two identical ARM processors or cores in the middle left of the chip and a PowerVR graphical processor unit (GPU) with four datapaths in the upper left quadrant. To the left and bottom side of the ARM cores are interfaces to main memory (DRAM). (Courtesy Chipworks, www.chipworks.com)
Apple A5
Notes: ARM is a RISC (reduced instruction set computing) processor, which requires significantly fewer transistors compared to a typical processor. Thus, it is relatively light weighted and consumes less power.

## Slide 21: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 22: Memory Hierarchy
L1/L2 Cache
Registers
Main Memory
Secondary Storage
Magnetic Tape
Typical Capacity
Typical Access Time
1 nanosecond
2 nanoseconds
10 nanoseconds
10 milliseconds
100 seconds
< 1 KB
32 KB/4 MB
1 – 16 GB
128 - 2000 GB
500 - 1000 GB

## Slide 23: Multi-core Chips
Two or more cores on a single chip
  How is this different from a true multi-processor?
    Shared components
      Cache (sometimes)
      Interconnect
    Cores can operate independently as with multi-processors
      But there will be contention for any shared resources
Fig: (a) A quad-core chip with a shared L2 cache (e.g. Intel).
(b) A quad-core chip with separate L2 caches (e.g. AMD).
Tanenbaum, Modern Operating Systems 3 e, (c) 2008 Prentice-Hall, Inc. All rights reserved. 0-13-6006639

## Slide 24: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface
The BIG Picture

## Slide 25: Instruction set architecture (ISA)
The hardware/software interface

## Slide 26: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 27: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 28: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
Year | Technology | Relative performance/cost | 
1951 | Vacuum tube | 1 | 
1965 | Transistor | 35 | 
1975 | Integrated circuit (IC) | 900 | 
1995 | Very large scale IC (VLSI) | 2,400,000 | 
2013 | Ultra large scale IC | 250,000,000,000 | 
DRAM capacity
§1.5 Technologies for Building Processors and Memory
Notes: 250,000,000,000 => 250 billions

## Slide 29: Manufacturing ICs
Yield: proportion of working dies per wafer
Self Study

## Slide 30: Intel Core i7 Wafer
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm
Self Study
Notes: Note: The diameter of an atom ranges from about 0.1 to 0.5 nanometers.

## Slide 31: Integrated Circuit Cost
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design
Self Study
Notes: The discussion of the cost estimation is important here because the cost of the integrated circuits is much of the cost of the PMD. Thus, computer designers must understand the costs of chips to understand the costs of current computer.
Equation (2) or Dies per wafer can be more accurately approximated as:
Dies per wafer = [(pi × (Wafer radius)^2.0) /Die_Area ] – [(pi × Wafer_radius) / (2 x Die_area)^0.5 ]

## Slide 32: Defining Performance
Which airplane has the best performance?
§1.6 Performance

## Slide 33: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll focus on response time for now…
Notes: Response time Also called execution time
Throughput Also called bandwidth
Answer:
Decreasing response time almost always improves throughput. Hence, in case 1, both response time and throughput are improved.
In case 2, no one task gets work done faster, so only throughput increases.

## Slide 34: Relative Performance
Define Performance = 1/Execution Time
“X is n time faster than Y”
Example: time taken to run a program
  10s on A, 15s on B
  Execution TimeB / Execution TimeA = 15s / 10s = 1.5
  So A is 1.5 times faster than B

## Slide 35: Measuring Execution Time
Elapsed time
  Total response time, including all aspects
    Processing, I/O, OS overhead, idle time
  Determines system performance
CPU time
  Time spent processing a given job
    Discounts I/O time, other jobs’ shares
  Comprises user CPU time and system CPU time
  Different programs are affected differently by CPU and system performance

## Slide 36: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock (cycles)
Data transfer and computation
Update state
Clock period
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz

## Slide 37
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE 1.1 The 2X vs. 10Y bytes ambiguity was resolved by adding a binary notation for all the common size terms. In the last column we note how much larger the binary term is than its corresponding decimal term, which is compounded as we head down the chart. These prefixes work for bits as well as bytes, so gigabit (Gb) is 109 bits while gibibits (Gib) is 230 bits.

## Slide 38: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 39: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 40: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 41: CPI Example
Computer A: Cycle Time = 250ps, CPI = 2.0
Computer B: Cycle Time = 500ps, CPI = 1.2
Same ISA
Which is faster, and by how much?
A is faster…
…by this much

## Slide 42: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 43: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 44: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture
Notes: CPU Time = [(Dynamic) Code-Size] x [CPI] x [Cycle-Time]

## Slide 45: Power Trends
In CMOS IC technology
§1.7 The Power Wall
×1000
×30
5V → 1V
Notes: 103 Watts power is the limit for transistors. If we go up, we basically burn all the transistors.
We can use additional coolers to lower the temperature of transistors, but it consumes so much power. PostPc era devices are dependable to the battery. Also, it is expensive.

## Slide 46: Reducing Power
Suppose a new CPU has
  85% of capacitive load of old CPU
  15% voltage and 15% frequency reduction
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 47: Uniprocessor Performance
§1.8 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 48: Uniprocessor Performance
RISC
Move to multi-processor
Notes: Opening a new era. People need to start coding multithreaded codes to improve their software performance.

## Slide 49: RISC-I: ~50,000 Transistors
Ref: http://www.cs.berkeley.edu/~pattrsn/Arch/RISC1.jpg
More: http://www.cs.berkeley.edu/~pattrsn/Arch/prototypes2.html
Notes: Ref: http://www.cs.berkeley.edu/~pattrsn/Arch/prototypes2.html,
http://www.cs.berkeley.edu/~pattrsn/Arch/RISC1.jpg

## Slide 50: Intel Core i7: ~700 million Transistors
Figure: Intel Nehalem Processor, Core i7.
Notes: Reference: http://download.intel.com/pressroom/kits/corei7/images/Nehalem_Die_Shot_3.jpg
Consists of 4 cores.
See http://en.wikipedia.org/wiki/List_of_Intel_Core_i7_microprocessors
According to Wikipedia, the largest transistor count in a commercially available single-chip processor is 19.2 billion AMD's Epyc

## Slide 51: Floor plan of Core i7
Notes: Reference: http://news.cnet.com

## Slide 52: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 53
Figure. (a) A three-stage pipeline. (b) A superscalar CPU.
Tanenbaum, Modern Operating Systems 3 e, (c) 2008 Prentice-Hall, Inc. All rights reserved. 0-13-6006639
Instruction level parallelism by pipelining
CPU cycle:
The basic cycle of every CPU is to fetch, decode and execute subsequent instructions. The cycle is repeated until the program finished.
Pipelining for efficiency:

## Slide 54: SPEC CPU Benchmark
Programs used to measure performance
  Supposedly typical of actual workload
Standard Performance Evaluation Corp (SPEC)
  Develops benchmarks for CPU, I/O, Web, …
SPEC CPU2006
  Elapsed time to execute a selection of programs
    Negligible I/O, so focuses on CPU performance
  Normalize relative to reference machine
  Summarize as geometric mean of performance ratios
    CINT2006 (integer) and CFP2006 (floating-point)
Notes: SPEC => Standard Performance Evaluation Cooperative
Benchmark is a measuring tool, special program which how long a computer takes the execute the program.
Idea: Use same benchmark in two different computer and compare their speed
Run the benchmark n times and take the geometric mean

## Slide 55: CINT2006 for Intel Core i7 920

## Slide 56: SPEC Power Benchmark
Power consumption of server at different workload levels
  Performance: ssj_ops/sec
  Power: Watts (Joules/sec)
Notes: ssj_ops => Server side Java operations per second.

## Slide 57: SPECpower_ssj2008 for Xeon X5650

## Slide 58: Fallacy: Low Power at Idle
Xeon X5650 power benchmark (slide# 60)
  At 100% load: 258W
  At 50% load: 170W (66%)
  At 10% load: 121W (47%)
Google data center
  Mostly operates at 10% – 50% load
  At 100% load less than 1% of the time
Consider designing processors to make power proportional to load
Notes: Note: (170W x 100%) / 258W = 65.89% = 66%
(121W X100%) / 258W = 46.89% = 47%

## Slide 59: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
§1.10 Fallacies and Pitfalls
  Can’t be done!
Example: multiply operation accounts for 80s of 100s in a program
  How much improvement in multiply performance to get 5× overall?
Corollary: make the common case fast
Notes: Pitfalls => are only true in limited context.

## Slide 60: Pitfall: MIPS as a Performance Metric
MIPS: Millions of Instructions Per Second
  Doesn’t account for
    Differences in ISAs between computers
    Differences in complexity between instructions
  CPI varies between programs on a given CPU

## Slide 61: Concluding Remarks
Performance/Cost is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance
§1.9 Concluding Remarks
Notes: You got to look ahead and see where is the future going and get there to be ready before it gets there
Dr. William Sawyer

## Slide 62: Q & A
(#1.5) Consider three different processors P1, P2, and P3 executing the same instruction set. P1 has a 3 GHz clock rate and a CPI of 1.5. P2 has a 2.5 GHz clock rate and a CPI of 1.0. P3 has a 4.0 GHz clock rate and has a CPI of 2.2.
  Which processor has the highest performance expressed in instructions per second?
Ans: performance of P1 (instructions/sec) = 3 × 109 / 1.5 = 2 × 109
performance of P2 (instructions/sec) = 2.5 × 109 / 1.0 = 2.5 x 109
performance of P3 (instructions/sec) = 4 × 109 / 2.2 = 1.8 × 109
        Thus, P2 > P1 > P3.
Notes: Note: we saw MIPS = (Clock-rate) / (CPI x 10^6), so here it should be = clock-rate / cpi

## Slide 63: Q & A (…1.5)
If the processors each execute a program in 10 seconds, find the number of cycles and the number of instructions.
Ans:
cycles(P1) = 10 × 3 × 109 = 30 × 109 cycles
cycles(P2) = 10 × 2.5 × 109 = 25 × 109 cycles
cycles(P3) = 10 × 4 × 109 = 40 × 109 cycles
No. instructions (P1) = 30 × 109/1.5 = 20 × 109
No. instructions (P2) = 25 × 109/1 = 25 × 109
No. instructions (P3) = 40 × 109/2.2 = 18.18 × 109
Notes: Execution time = Cycles / clock-rate
Or, Cycles = Exe-time x clock-rate

## Slide 64: Q & A (…1.5)
We are trying to reduce the time by 30% but this leads to an increase of 20% in the CPI. What clock rate should we have to get this time reduction?
Ans:
CPInew = CPIold × 1.2,
  then CPI(P1) = 1.8, CPI(P2) = 1.2, CPI(P3) = 2.64.
Clock-rate, f = No. instr. × CPI/time, then
f (P1) = (2 × 109 ×1.8)/ (0.7) = 5.14 GHz
f (P2) = (2.5 × 109 × 1.2) / (0.7) = 4.28 GHz
f (P3) = (1.8 × 109 × 2.64) / (0.7) = 6.78 GHz
Notes: Or, You can solve as following for P1:
CPI_new = CPI_old 1.2
CPU_Time_new = 0.7 CPU_Time_old
Clock-rate_new = ? Clock-rate_old = 3GHz
I x CPI_new 1.2 x CPI_old
Clock-rate_new ---------------------------- -----------------------
CPU_Time_New 0.7 CPU_Time_old 1.2
------------------- = -------------------------------- = ----------------------------- = -------
I x CPI_old CPI_old 0.7
Clock-rate_old ---------------------------- -------------------------
CPU_Time_old CPU_Time_old
1.2 1.2
=> Clock-rate_new = ------ x Clock-rate_old = -------- x 3 GHz = 5.142 … GHz
0.7 0.7

## Slide 65: Q & A
(#1.6) Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, and D). P1 with a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3, and P2 with a clock rate of 3 GHz and CPIs of 2, 2, 2, and 2.
Given a program with a dynamic instruction count of 1.0E6 instructions divided into classes as follows: 10% class A, 20% class B, 50% class C, and 20% class D, which implementation is faster?
  What is the global CPI for each implementation?
Notes: Note: The dynamic instruction count is the actual number of instructions executed by the CPU for a specific program execution.
and the static instruction count is the number of instruction the program has.

## Slide 66: Q & A (… 1.6)
Class A: 105 instr. [Since 10% of 106 = 105]
Class B: 2 × 105 instr. [Since 20% of 106 = 2 × 105, etc.]
Class C: 5 ×105 instr.
Class D: 2 × 105 instr.
Time = No. instr. × CPI/clock rate
Total time P1 = (105 + 2 ×105 × 2 + 5 × 105 × 3 + 2 × 105 × 3)/(2.5 ×109) = 10.4 × 10-4 s
Total time P2 = (105 × 2 + 2 × 105 × 2 + 5 × 105 × 2 + 2 × 105 × 2)/(3 × 109) = 6.66 × 10-4 s
CPI (P1) = 10.4 × 10-4 × 2.5 × 109/106 = 2.6 [Since, Time = Cycles × Cycle-time,]
CPI (P2) = 6.66 × 10-4 × 3 × 109/106 = 2.0 [therefore, Cycles = Time × Clock-rate]
Notes: Alternatively:
Total Clock-Cycle 1, CC1 =  (I x CPI) = (105 + 2 ×105 × 2 + 5 × 105 × 3 + 2 × 105 × 3) = (1+4+15+6) x 105= 26 x 105
Total Clock-Cycle 2, CC2 =  (I x CPI) = (105 × 2 + 2 × 105 × 2 + 5 × 105 × 2 + 2 × 105 × 2) = (2+4+10+4) x 105= 20 x 105
Global or Average CPI1 = CC1 / Total Instructions (I) = (26 x 105)/ 106= 2.6.
Global or Average CPI1 = CC2 / Total Instructions (I)= (20 x 105)/ 106= 2.0.

## Slide 67: Q & A (… 1.6)
Find the clock cycles required in both cases.
Ans:
Since, CPI × No. Instr = Cycles, therefore,
clock cycles (P1) = 105 × 1+ 2 × 105 × 2 + 5 × 105 × 3 + 2 × 105 × 3 = 26 × 105
clock cycles (P2) = 105 × 2 + 2 × 105 × 2 + 5 × 105 × 2 + 2 × 105 × 2 = 20 × 105

## Slide 68: Q & A
Notes: 1.5 / 1.2 = 1.25

## Slide 69: Q & A (… 1.7)
Notes: Note: Ta(exec)= Tb(exec)
[CPIa x Ia/fa] = [CPIb x Ib/fb]
fb/fa = [CPIb x Ib] / [CPIa x Ia]
fb/fa = 1.37
==================
[CPIb x Ib] / CRb Tb/Tn = -------------------------- [CPIn x In] / CRn [Note: CRb=CRn] [CPIb x Ib] = ------------------------ [CPIn x In] 1.25 x 1.2 E9 = ------------------ 1.1 x 6E8 1.5 x E9 15 = ---------------- = --------- = 2.27... 6.6 x E8 6.6

## Slide 70: Q & A

## Slide 71: Q & A (… 1.8)
b. For each processor, find the percentage of the consumed static power with respect to the total consumed power.
.
Pentium 4: 10/100 = 10%
Core i5 Ivy Bridge: 30/70 = 42.9%

## Slide 72: Q & A
Q: How did the development of the transistor affect computers? What did the transistor replace?
Ans:
The development of transistor has had a tremendous impact on bringing the computer to our homes in the form of PCs and more recently into our hands (Personal Digital Assistants etc). The ability to package and integrate transistors on a chip at a rate that has been increasing exponentially according to Moore’s Law has resulted in tremendous performance gains for programs without having to change any of them.
The transistor replaced the vacuum tube in 1951.

## Slide 73: Q & A
(Amdahl’s law question) suppose you have a machine which executes a program consisting of 50% floating point multiply, 20% floating point divide, and the remaining 30% are from other instructions.
(a) Management wants the machine to run 4 times faster. You can make the divide run at most 3 times faster and the multiply run at most 8 times faster. Can you meet management’s goal by making only one improvement, and which one?
Ans: (a) Amdahl’s Law states:
Execution time after improvement =
(Execution time affected by improvement)/(Amount of Improvement) +
Execution time unaffected.

## Slide 74: Q & A
Assuming initially that the floating point multiply, floating point divide and the other instructions had the same CPI:
i) Execution time after Improvement with Divide = (20)/3 + (50 + 30) = 86.67
ii) Execution time after Improvement with Multiply = (50)/8 + (20 + 30) = 56.25
So what do you think?
(b) Bob has now taken over the company removing all the previous managers. If you make both the multiply and divide improvements, what is the speed of the improved machine relative to the original machine?
If we make both the improvements,
Execution time after Improvement = (50)/8 + (20)/3 + (30) = 42.91
The speedup relative to the original machine = (100)/(42.91) = 2.33