## Slide 1: CSCI-3301-Chapter 3
Arithmetic for Computers
Abdullah Yasin Nur

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 4
Half-Adders
Basic rules of binary addition are performed by a half adder, which accepts two binary inputs (A and B) and provides two binary outputs (Carry-out and Sum).
The logic symbol and equivalent circuit are:

## Slide 5
Full-Adders
A full adder accepts three binary inputs (A, B, and Carry-in) and provides two binary outputs (Carry-out and Sum). The truth table summarizes the operation.
A full-adder can be constructed from two half adders as shown:

## Slide 6
Full-Adders
A
B
S
Cout
S
A
B
S
Cout
S
For the given inputs, determine the intermediate and final outputs of the full adder.
1
1
0
1
0
The first half-adder has inputs of 1 and 0; therefore the Sum =1 and the Carry out = 0.
The second half-adder has inputs of 1 and 1; therefore the Sum = 0 and the Carry out = 1.
The OR gate has inputs of 1 and 0, therefore the final carry out = 1.
1
0
1
Sum
Cout

## Slide 7: Integer Subtraction
Add negation of second operand
For negative operand, use 2’s complement
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Remember 2’s complement
  Complement each bit (1 to 0, 0 to 1) and add 1
  6 = 0000 0000 0000 0000 0000 0000 0000 0110
  -6 = 1111 1111 1111 1111 1111 1111 1111 1010

## Slide 8: Integer Subtraction
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 9: Overflow conditions for addition and subtraction
Case 1
A = 0111 0000 0000 0000 0000 0000 0000 0000
B = 0101 0000 0000 0000 0000 0000 0000 0000
Sum = 1100 0000 0000 0000 0000 0000 0000 0000
Case 2
A = 1111 0000 0000 0000 0000 0000 0000 0000
B = 1000 1000 0000 0000 0000 0000 0000 0000
Sum = 0111 1000 0000 0000 0000 0000 0000 0000
Case 1
A = 1879048192
B = 1342177280
Sum = -1073741824
Case 2
A = -268435456
B = -2013265920
Sum = 2013265920

## Slide 10: Overflow conditions for addition and subtraction
Case 3
A = 0111 0000 0000 0000 0000 0000 0000 0000
B = 1101 0000 0000 0000 0000 0000 0000 0000
A = 0111 0000 0000 0000 0000 0000 0000 0000
B” = 0011 0000 0000 0000 0000 0000 0000 0000
Sum = 1010 0000 0000 0000 0000 0000 0000 0000
Case 3
A = 1879048192
B = -805306368
Sub = -1610612736

## Slide 11: Overflow conditions for addition and subtraction
Case 4
A = 1111 0000 0000 0000 0000 0000 0000 0000
B = 0101 0000 0000 0000 0000 0000 0000 0000
A = 1111 0000 0000 0000 0000 0000 0000 0000
B” = 1011 0000 0000 0000 0000 0000 0000 0000
Sum = 0010 0000 0000 0000 0000 0000 0000 0000
Case 3
A = -268435456
B = 1342177280
Sub = 536870912

## Slide 12: Dealing with Overflow in MIPS
We have seen that signed and two’s complement case(s) where overflow can occur.
For unsigned: since it is commonly used for memory addressing the overflows are ignored.
Thus, MIPS provides 2 choices:
  Use add, addi and sub which cause exceptions on overflow.
  Or, to use addu, addui and subu instructions which do not cause exception on overflow.

## Slide 13: Dealing with Overflow …
Some languages (e.g., C, Java) ignore overflow
Other languages (e.g., Ada, Fortran) require raising an exception

## Slide 14: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Max length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication
Notes: Note: for length-theory of the multiplier, check with decimal 99 x 99 = 9801,
Or for Hex, FF x FF =FE01.
Or, binary 1011 x 1101 = (11 x 13 in decimal) = 1000 1111 (143 in decimal)

## Slide 15: Multiplication Hardware
Initially 0
If each operations requires one clock cycle, then for 3 operations applied to each 32 bits will require almost 100 clock cycle in total.
If these 3 operations are done in parallel then it will require 1/3 of this execution time.
First number
Second number

## Slide 16: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 17: Signed Multiplier
Convert the multiplier and multiplicand to positive numbers and remember the original signs.
Run for 31 iterations, leaving the signs out of calculation.
If the signs disagree then we need to negate the result.
Shifting steps extend the sign of product for signed numbers.
Finally, the lower word will have the 32-bit product.

## Slide 18: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 19: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division
Self Study

## Slide 20: Division Hardware
Initially dividend
Initially divisor in left half
Self Study

## Slide 21: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both
Here, quotient is in the right half of the remainder register.
Self Study

## Slide 22: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder ( rs mod rt)
  LO: 32-bit quotient ( rs / rt )
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 23
The Binary Number System
The binary number system is used in digital systems. Binary has only two symbols that are used to represent quantities: 0 and 1.
The column weights of binary numbers are powers of two that increase from right to left beginning with 20 =1:
… 25 24 23 22 21 20.
For fractional binary numbers, the column weights are negative powers of two that decrease from left to right:
… 22 21 20 . 2-1 2-2 2-3 2-4 …

## Slide 24
Binary Weights
The positional weights for binary numbers are assigned as shown below.

## Slide 25
Binary-to-Decimal Conversion
The decimal equivalent of a binary number can be determined by adding the column values of all of the bits that are 1 and discarding all of the bits that are 0.
Convert the binary number 100101.01 to decimal.
Start by writing the column weights; then add the weights that correspond to each 1 in the number.
25 24 23 22 21 20. 2-1 2-2
32 16 8 4 2 1 0.5 0.25
1 0 0 1 0 1. 0 1
32 +4 +1 +0.25 =
37.25

## Slide 26
Decimal-to-Binary Conversions
You can convert a decimal whole number to binary by reversing the procedure. Write the decimal weight of each column and place 1’s in the columns that sum to the decimal number.
Convert the decimal number 49 to binary.
The column weights double in each position to the right. Write down column weights until the last number is larger than the one you want to convert.
26 25 24 23 22 21 20
64 32 16 8 4 2 1
0 1 1 0 0 0 1

## Slide 27
Decimal-to-Binary Conversions
You can convert a decimal fraction to binary by repeatedly multiplying the fractional results of successive multiplications by 2. The carries form the binary number.
Continue to the desired number of decimal places or stop when the fractional part is all zeros.

## Slide 28: Floating Point
Representation for non-integer numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 29: Floating Point
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 30: Floating Point Standard
Defined by IEEE Std 754
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 31: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
1 + Fraction to make sure the number is scientific format.
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 32: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 33: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 34: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value (Normalized case)
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 35: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value (Normalized case)
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 36: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 37: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 38: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 =>(0.5 + –0.4375)10
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) => 0.0625

## Slide 39: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4
Self Study
Notes: Note: Step 2 is “Add significands”

## Slide 40: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined
Self Study

## Slide 41: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize (if necessary)
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 42: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 => (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3 (Real exponent)
  Biased: (–1 + –2) + 127 => –3 + 127 = 124
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 43: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined
Self Study

## Slide 44
44
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE: Floating-point multiplication. The normal path is to execute steps 3 and 4 once, but if rounding causes the sum to be unnormalized, we must repeat step 3.
Floating-point multiplication
Self Study

## Slide 45: FP Instructions in MIPS
FP hardware is coprocessor 1
  Adjunct processor that extends the ISA
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Release 2 of MIPs ISA supports 32 × 64-bit FP reg’s
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  lwc1, ldc1, swc1, sdc1
    e.g., ldc1 $f8, 32($sp)
Notes:     Note: “ldc1 $f8, 32($sp)” is a 64 bit operation (since it is ‘ld’ or ‘load double’) so, another register will be needed with $f8 and it should be $f9 – it is basically ‘even-odd’ pair.

## Slide 46: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, neq, lt, le, gt, ge)
  Sets FP condition-code bit (if correct “true”, otherwise “false”)
    e.g. c.lt.s $f3, $f4
Branch on FP condition code true or false
  Bc1t (branch if true), bc1f (branch if false)
    e.g., bc1t TargetLabel
Notes: c. => compare
c.lt.d $f0, $f2 # condition code = $f0 < $f2
bc1t TargetLabet #Branch if $f0 < $f2 is TRUE

## Slide 47: FP Instructions in MIPS
Conditional jumps are performed in two stages
  Comparison of FP values sets a code in a special register
  Branch instructions jump depending on the value of the code
Comparison
  c.eq.s $f2, $f4 #(if $f2 == $f4 then code = 1 else code = 0)
  c.le.s $f2, $f4 #(if $f2 <= $f4 then code = 1 else code = 0)
  c.lt.s $f2, $f4 #(if $f2 < $f4 then code = 1 else code = 0)
Branches
  bc1f label #(if code == 0 then jump to label)
  bc1t label #(if code == 1 then jump to label)

## Slide 49: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in $f12, result in $f0, literals in global memory space
Compiled MIPS code:
f2c: lwc1 $f16, const5($gp) #$f16 = 5.0 lwc1 $f18, const9($gp) #$f18 = 9.0 div.s $f16, $f16, $f18 #$f16 = 5.0/9.0 lwc1 $f18, const32($gp)#$f18= 32.0 sub.s $f18, $f12, $f18 #$f18=fahr-32.0 mul.s $f0, $f16, $f18 #$f0= output result jr $ra

## Slide 50: FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k; for (i = 0; i! = 32; i = i + 1) for (j = 0; j! = 32; j = j + 1) for (k = 0; k! = 32; k = k + 1) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in $a0, $a1, $a2, and i, j, k in $s0, $s1, $s2
Self Study
Notes: mm = matrix mult.

## Slide 51: FP Example: Array Multiplication
MIPS code:
li $t1, 32 # $t1 = 32 (row size/loop end) li $s0, 0 # i = 0; initialize 1st for loop L1: li $s1, 0 # j = 0; restart 2nd for loop L2: li $s2, 0 # k = 0; restart 3rd for loop sll $t2, $s0, 5 # $t2 = i * 32 (size of row of x) addu $t2, $t2, $s1 # $t2 = i * size(row) + j sll $t2, $t2, 3 # $t2 = byte offset of [i][j] addu $t2, $a0, $t2 # $t2 = byte address of x[i][j] l.d $f4, 0($t2) # $f4 = 8 bytes of x[i][j] L3: sll $t0, $s2, 5 # $t0 = k * 32 (size of row of z) addu $t0, $t0, $s1 # $t0 = k * size(row) + j sll $t0, $t0, 3 # $t0 = byte offset of [k][j] addu $t0, $a2, $t0 # $t0 = byte address of z[k][j] l.d $f16, 0($t0) # $f16 = 8 bytes of z[k][j] …
Self Study

## Slide 52: FP Example: Array Multiplication
… sll $t0, $s0, 5 # $t0 = i*32 (size of row of y) addu $t0, $t0, $s2 # $t0 = i*size(row) + k sll $t0, $t0, 3 # $t0 = byte offset of [i][k] addu $t0, $a1, $t0 # $t0 = byte address of y[i][k] l.d $f18, 0($t0) # $f18 = 8 bytes of y[i][k] mul.d $f16, $f18, $f16 # $f16 = y[i][k] * z[k][j] add.d $f4, $f4, $f16 # f4=x[i][j] + y[i][k]*z[k][j] addiu $s2, $s2, 1 # $k k + 1 bne $s2, $t1, L3 # if (k != 32) go to L3 s.d $f4, 0($t2) # x[i][j] = $f4 addiu $s1, $s1, 1 # $j = j + 1 bne $s1, $t1, L2 # if (j != 32) go to L2 addiu $s0, $s0, 1 # $i = i + 1 bne $s0, $t1, L1 # if (i != 32) go to L1
Self Study

## Slide 53: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements
Notes: IEEE 754 offers several modes of rounding to let the programmer pick the desired approximation.
For rounding hardware holds extra bits in calculation (which can be used in the intermediate calculation).
If your intermediate result had to be truncated to the exact number of digits, there would be no opportunity to round.
Thus, IEEE 754 keeps two extra bit on the right during intermediate additions, called guard(G) and round (R), respectively.
Sticky bit allows the computer to see the difference between 0.50…00 (decimal) and 0.50…01 (decimal).

## Slide 54: Accurate Arithmetic
Example: Rounding with Guard Digits
  Add 2.56ten x 100 to 2.34ten x 102
  Assume, we have 3 significant decimal digits
With guard and round digits | Without guard and round digits
2.3400ten + 0.0256ten ------------------------ 2.3656ten Thus, sum = 2.3656ten x 102. Here, we have two digits to round: we can round down 0 to 49 and round up 51 to 99, while 50 is the tiebreaker. Thus, finally, sum =2.37ten x 102. | 2.34ten + 0.02ten ------------------------ 2.36ten Thus, sum = 2.36ten x 102. Here, the final sum remains the same, that is 2.36ten x 102.

## Slide 55: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)
§3.6 Parallelism and Computer Arithmetic: Subword Parallelism
Self Study

## Slide 56: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance
§3.7 Real Stuff: Streaming SIMD Extensions and AVX in x86
Self Study

## Slide 57: x86 FP Instructions
Optional variations
  I: integer operand
  P: pop operand from stack
  R: reverse operand order
  But not all combinations allowed
Data transfer | Arithmetic | Compare | Transcendental
FILD mem/ST(i) FISTP mem/ST(i) FLDPI FLD1 FLDZ | FIADDP mem/ST(i) FISUBRP mem/ST(i) FIMULP mem/ST(i) FIDIVRP mem/ST(i) FSQRT FABS FRNDINT | FICOMP FIUCOMP FSTSW AX/mem | FPATAN F2XMI FCOS FPTAN FPREM FPSIN FYL2X
Self Study

## Slide 58: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data
Self Study

## Slide 59: Matrix Multiply
Unoptimized code:
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n]; /* cij = C[i][j] */
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n]; /* cij += A[i][k]*B[k][j] */
9. C[i+j*n] = cij; /* C[i][j] = cij */
10. }
11. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Self Study

## Slide 60: Matrix Multiply
x86 assembly code:
1. vmovsd (%r10),%xmm0 # Load 1 element of C into %xmm0
2. mov %rsi,%rcx # register %rcx = %rsi
3. xor %eax,%eax # register %eax = 0
4. vmovsd (%rcx),%xmm1 # Load 1 element of B into %xmm1
5. add %r9,%rcx # register %rcx = %rcx + %r9
6. vmulsd (%r8,%rax,8),%xmm1,%xmm1 # Multiply %xmm1, element of A
7. add $0x1,%rax # register %rax = %rax + 1
8. cmp %eax,%edi # compare %eax to %edi
9. vaddsd %xmm1,%xmm0,%xmm0 # Add %xmm1, %xmm0
10. jg 30 <dgemm+0x30> # jump if %eax > %edi
11. add $0x1,%r11d # register %r11 = %r11 + 1
12. vmovsd %xmm0,(%r10) # Store %xmm0 into C element
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Self Study

## Slide 61: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i+=4 )
5. for ( int j = 0; j < n; j++ ) {
6. __m256d c0 = _mm256_load_pd(C+i+j*n); /* c0 = C[i][j] */
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, /* c0 += A[i][k]*B[k][j] */
9. _mm256_mul_pd(_mm256_load_pd(A+i+k*n),
10. _mm256_broadcast_sd(B+k+j*n)));
11. _mm256_store_pd(C+i+j*n, c0); /* C[i][j] = c0 */
12. }
13. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Self Study

## Slide 62: Matrix Multiply
Optimized x86 assembly code:
1. vmovapd (%r11),%ymm0 # Load 4 elements of C into %ymm0
2. mov %rbx,%rcx # register %rcx = %rbx
3. xor %eax,%eax # register %eax = 0
4. vbroadcastsd (%rax,%r8,1),%ymm1 # Make 4 copies of B element
5. add $0x8,%rax # register %rax = %rax + 8
6. vmulpd (%rcx),%ymm1,%ymm1 # Parallel mul %ymm1,4 A elements
7. add %r9,%rcx # register %rcx = %rcx + %r9
8. cmp %r10,%rax # compare %r10 to %rax
9. vaddpd %ymm1,%ymm0,%ymm0 # Parallel add %ymm1, %ymm0
10. jne 50 <dgemm+0x50> # jump if not %r10 != %rax
11. add $0x1,%esi # register % esi = % esi + 1
12. vmovapd %ymm0,(%r11) # Store %ymm0 into 4 C elements
§3.8 Going Faster: Subword Parallelism and Matrix Multiply
Self Study

## Slide 63: Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift (sra): replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  c.f. 111110112 >>> 2 = 001111102 = +62 (srl)
§3.9 Fallacies and Pitfalls
Notes: NOTE:
srl: shift right logical, >>>
sra: shift right arithmetic, >>

## Slide 64: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 65: Who Cares About FP Accuracy?
Notes: ⊺ Ref: wiki

## Slide 66
Notes: ⊺ Ref: wiki

## Slide 67: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
§3.9 Concluding Remarks

## Slide 68: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow
MIPS ISA
  Core instructions: 54 most frequently used
    100% of SPECINT, 97% of SPECFP
  Other instructions: less frequent
        --- x ---