## Slide 1: Chapter 4
The Processor
Abdullah Yasin Nur

## Slide 2: Review: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats
Notes: x86, variable instruction set: 1 to 17 bytes in length

## Slide 3: The Processor Design
We will examine two MIPS implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: lw, sw
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq, j
§4.1 Introduction

## Slide 4: MIPS R-format Instructions
Instruction fields
  op: Basic operation of the instruction, called opcode or operation code.
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Review

## Slide 5: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
See Appendix A for other instructions …
Review

## Slide 6: MIPS I-format Instructions
Note: in a load instruction, the rt field specifies the destination register, which receives the result of the load.
Based on op, hardware can uniquely identify instructions among various formats.
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
FIGURE: MIPS instruction encoding. In the table above, “reg” means a register number between 0 and 31, “address” means a 16-bit address. Note that add and sub instructions have the same value in the op field; the hardware uses the funct field to decide the variant of the operation: add (32) or subtract (34).
Review

## Slide 7: Translating MIPS to Machine Language
Example: A [300] = h + A [300];
If $t1 has the base of A and $s2 maps to h
then MIPS code can be
  lw $t0, 1200($t1)
  add $t0, $s2, $t0
  sw $t0, 1200($t1)
The corresponding machine code (in decimal) can be as following:
The corresponding machine code (in binary) can be as following:
Review

## Slide 8
8
Copyright © 2014 Elsevier Inc. All rights reserved.
FIGURE: MIPS instruction formats: R, I, J.
3 MIPS Instructions format: R, I, J
Review

## Slide 9: Instruction Execution
For every instructions, the first 2 steps are same:
1. Send the PC to the memory and fetch the instruction from that memory:
  PC  instruction memory, fetch instruction
2. All instructions read one or two registers (except j):
  Register numbers  register file, read registers
After the above 2 steps, depending on instruction class:
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 10: CPU Overview
Figure: An abstract view of the implementation of the MIPS subset showing the major functional units and the major connections between them.
All instructions start by using the program counter to supply the instruction address to the instruction memory. After the instruction is fetched, the register operands used by an instruction are specified by fields of that instruction. Once the register operands have been fetched, they can be operated on to compute a memory address (for a load or store), to compute an arithmetic result (for an integer arithmetic-logical instruction), or a compare (for a branch). If the instruction is an arithmetic-logical instruction, the result from the ALU must be written to a register. If the operation is a load or store, the ALU result is used as an address to either store a value from the registers or load a value from memory into the registers. The result from the ALU or memory is written back into the register file. Branches require the use of the ALU output to determine the next instruction address, which comes either from the ALU (where the PC and branch offset are summed) or from an adder that increments the current PC by 4. The thick lines interconnecting the functional units represent buses, which consist of multiple signals. The arrows are used to guide the reader in knowing how information flows. Since signal lines may cross, we explicitly show when crossing lines are connected by the presence of a dot where the lines cross.

## Slide 11: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 12: Mux (Multiplexer)
FIGURE: A two-input multiplexor on the top and its implementation with gates on the bottom. The multiplexor has two data inputs (A and B), which are labeled 0 and 1, and one selector input (S), as well as an output C.

## Slide 13: Control
FIGURE: The basic implementation of the MIPS subset, including the necessary multiplexors and control lines.
The top multiplexor (“Mux”) controls what value replaces the PC (PC + 4 or the branch destination address); the multiplexor is controlled by the gate that “ANDs” together the Zero output of the ALU and a control signal that indicates that the instruction is a branch.
The added control lines are straightforward and determine the operation performed at the ALU, whether the data memory should read or write, and whether the registers should perform a write operation. The control lines are shown in color to make them easier to see.
The middle multiplexor, whose output returns to the register file, is used to steer the output of the ALU (in the case of an arithmetic-logical instruction) or the output of the data memory (in the case of a load) for writing into the register file.
Finally, the bottommost multiplexor is used to determine whether the second ALU input is from the registers (for an arithmetic-logical instruction or a branch) or from the offset field of the instruction (for a load or store).
Notes: Note: Zero output in ALU indicates if all Result lines have value 0 (See appendix B for more)

## Slide 14: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Datapath elements in MIPS are of 2 types:
  1. Combinational element (output depends only on the current inputs)
    Operate on data
    Output is a function of input
  2. State (sequential) elements
    Store information: instruction, data memory, reg. …

## Slide 15: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 16: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 17: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a MIPS datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 18: Instruction Fetch
32-bit register
Increment by 4 for next instruction
Program counter + Instruction memory + Adder

## Slide 19: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result
R instruction class includes: add, sub, AND, OR, slt, …
Notes: Zero is 1-bit signal, indicate when the result is 0.

## Slide 20: Load/Store Instructions
General form of load/store:
lw $t1, offset_value($t2) # load word; offset is of 16 bits
sw $t1, offset_value($t2) # store word; $t2 is the base reg.
Read register operands
Calculate address using 16-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 21: Branch Instructions
Example: beq $t1, $t2, offset # 16-bits offset
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 22: Branch Instructions
Just re-routes wires
Sign-bit wire replicated
Need to do 2 operations:
Compute the branch target address.
Compare the register contents.
Separate adder

## Slide 23: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 24: R-Type/Load/Store Datapath
While instruction/1 clock cycle: no datapath resource can be used more than once per instruction,
so any element needed more than once must be duplicated.
Thus, we need a memory for instructions separate from one for data.

## Slide 25: Full Datapath

## Slide 26: Control
Slide 13 – Recall
Notes: Note: Zero output in ALU indicates if all Result lines have value 0 (See appendix B for more)

## Slide 27: Building ALU & its Control
We construct a simple ALU from 5 basic hardwares:
  AND & OR gates, inverters, multiplexors and full adder
  In reality, ALU contains more hardware e.g. multiplication
  (Read Appendix B for more details)
FIGURE 1: The 1-bit logical unit for AND and OR.
FIGURE 2: A 1-bit adder. This adder is called a full adder; it is also called a (3,2) adder because it has 3 inputs and 2 outputs. An adder with only the a and b inputs is called a (2,2) adder or half-adder.

## Slide 28: … Building ALU & its Control
A 1 bit ALU that performs:
  AND, OR and Addition
Operation: => Control
AND=> 00
OR => 01
Add => 10
Figure: A 1-bit ALU that performs AND, OR, and Addition and selection them with control bits 00, 01 and 10 respectively.

## Slide 29: … Building ALU & its Control
Remember 2’s complement

## Slide 30: … Building ALU & its Control

## Slide 31: … Building ALU & its Control

## Slide 32: … Building ALU & its Control
Set Less Than (slt) Function:
e.g. slt $t0, $t1, $t2 # if t1 < t2 then t0 = 1 else t0 = 0
  Defined as:
    000 … 001 or, 1 for A < B
    A slt B =
    000 … 000 or, 0 for A ≥ B
  Logic: When subtract b from a, if the difference is negative then a < b, since (a-b) < 0.
  We want the LSB of slt operation to be ‘1’ if (a-b) < 0 and ‘0’ otherwise.
Output:

## Slide 33: … Building ALU & its Control

## Slide 34: … Building ALU & its Control
A 32-bit ALU constructed from the 31 copies of the 1-bit ALU in Figure 1 of previous slide and one 1-bit ALU in Figure 2 of previous slide.
All the ‘Less’ inputs are connected to 0 except for the least significant bit, which is connected to the ‘Set’ output of the most significant bit.
If the ALU performs (a – b) and we select the input 3 in the multiplexor as shown in the Figure, then Result = 000 … 001 if a < b, and Result = 000 … 000 otherwise.
32 bit slt:
Note:
Every time we want the ALU to subtract, we set both CarryIn and Binvert to 1.
For add or logic operation we want both CarryIn and Binvert to 0.

## Slide 35: ALU Control
ALU used for the following functions (F):
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR
To choice the above R-Type functions (except NOR), the three ALU control lines, Ainvert, Bnegate, and the operations are used.
For lw/sw add is used to compute the memory address.
For branch equal (beq), the ALU performs a subtraction.

## Slide 36: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add
(type i)
(type i)
Base reg.
(dest.)
Notes: Note: (dest.)
For load instruction the destination register’s bit positions are 20:16 (rt), while for an R-type instruction it is in bit positions 15:11 (rd).
Thus we will need a multiplexor to select which field of the instruction is used to indicate the register number to be written.

## Slide 37: Datapath With Control

## Slide 38: R-Type Instruction

## Slide 39: Load Instruction

## Slide 40: Branch-on-Equal Instruction

## Slide 41: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of current PC+4
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 42: Datapath With Jumps Added

## Slide 43: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 44: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.29
Non-stop:
  Speedup ≈ 4 = number of stages
Notes: Sequential 4 loads take 8 hrs., whereas the 4 loads in pipeline take 3.5 hrs. So the speedup is 8/3.5 = 2.29.

## Slide 45: MIPS Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 46: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 47: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)
Important: We assume, that the register file is read during the second half of the clock cycle and the register file is written in the first half of the clock cycle.
Notes: Important Note:
We assume, that the register file is read during the second half of the clock cycle and the register file is written in the first half of the clock cycle.

## Slide 48: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 49: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 50: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 51: Structure Hazards
Conflict for use of a resource
  Assume, you have a washer & dryer combined machine instead of separate. So, your cannot do both the job in parallel.
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
Notes: Structural Hazard => When a planned instruction cannot execute in the proper clock cycle because the hardware does not support the combination of instructions that are set to execute.

## Slide 52: Structure Hazards
  4th instruction
With the 4th instruction, we see that in the same clock cycle:
(1) the 1st instruction is accessing data from memory (highlighted green) while if
(2) the 4th instruction is fetching instruction from the same memory (highlighted red)
that would have caused structural hazard.
1st instruction
Notes: Structural Hazard => When a planned instruction cannot execute in the proper clock cycle because the hardware does not support the combination of instructions that are set to execute.

## Slide 53: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1 sub $t2, $s0, $t3
Notes: Note:
White Box => Not in use by the instruction.
Box with shed in the Right part => (used and ) a read operation.
Box with shed in the Left part => (used and ) a write operation.
Grey Box / Shaded Box => in use.

## Slide 54: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 55: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
Unavoidable Stall

## Slide 56: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles
Notes: Looking at the code we can say:
B is in memory location 0($t0);
E is in memory location 4($t0);
A is in memory location 12($t0);
F is in memory location 8($t0);
C is in memory location 16($t0);

## Slide 57: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In MIPS pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 58: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 59: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 60: MIPS with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 61: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 62: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 63: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards
Notes: Note: Flow from right to left (R-L) is a problem for the next instruction. And there are two R-L flows:
WB to Reg: can cause data hazard
PC1 to PC2: can lead to control hazard

## Slide 64: MIPS Pipelined Datapath
§4.6 Pipelined Datapath and Control
Figure: each instruction has its own data-path, and shades each portion according to use. Each stage is labeled by the physical resource
IM represents the instruction memory and the PC in the instruction fetch stage,
Reg stands for the register file and sign extender in the instruction decode/register file read stage (ID), and so on.
Note: To maintain proper time order, the datapath breaks the register file into two logical parts: registers read during register fetch (ID) and registers written during write back (WB). We already assumed that the register file is written in the first half of the clock cycle and the register file is read during the second half.
Main Message:
The figure above seems to suggest that the 3 separate instructions need 3 private datapath – instead, we add register to hold data so that portions of a single datapath can be shared during instruction executions.

## Slide 65: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle
Notes: Q1: Why there is no pipeline register at the end of the write-back (WB) state?
A1: All instructions must update some stage in the processor, such as, register file, memory, or the PC – so a separate pipeline register is redundant to the state that is updated.
For example, a load instruction will place its result in 1 of 32 registers, and any later instruction that needs that data will simply read the appropriate register.
Of course, PC can be thought of a pipeline register: every instruction updates the PC, whether by incrementing it or by setting it to branch destination address.

## Slide 66: IF for Load, Store, …

## Slide 67: ID for Load, Store, …

## Slide 68: EX for Load

## Slide 69: MEM for Load

## Slide 70: WB for Load
Wrong register number

## Slide 71: Corrected Datapath for Load

## Slide 72: EX for Store

## Slide 73: MEM for Store

## Slide 74: WB for Store
Note: 5th stage (WB) is doing nothing for SW’s execution.

## Slide 75: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 76: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 77: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 78: Pipelined Control (Simplified)

## Slide 79: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 80: Pipelined Control

## Slide 81: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 # Reg. $2 written by sub and $12,$2,$5 # 1st operand ($2) depends on sub or $13,$6,$2 # 2nd operand ($2) depends on sub add $14,$2,$2 # 1st ($2) & 2nd ($2) depend on sub sw $15,100($2) # Base ($2) depends on sub
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling
Notes: Note:
** All the last 4 instructions are dependent on the result in register $2 of the first instruction.
** If register $2 had a value 10 before the subtract instruction and became -20 afterwards, the programmer intends that -20 will be used in the following instructions that refer to register $2.

## Slide 82: Dependencies & Forwarding
Notes: Assume the value of $2 was 10 before and -20 after the execution of the 1st instruction.
Red connections are forwarding – which is a solution here without stall.

## Slide 83: Dependencies & Forwarding
Figure 1: (c) We assume that the register file forwards values that are read and written during the same clock cycle, so the add does not stall, but the values come from the register file instead of a pipeline register. Register file “forwarding”—that is, the read gets the value of the write in that clock cycle—is why clock cycle 5 shows register $2 having the value 10 at the beginning and −20 at the end of the clock cycle. As in the rest of this section, we handle all forwarding except for the value to be stored by a store instruction.
Figure 1: (a) The dependences between the pipeline registers move forward in time, so it is possible to supply the inputs to the ALU needed by the AND instruction and OR instruction by forwarding the results found in the pipeline registers.
Figure 1: (b) The values in the pipeline registers show that the desired value is available before it is written into the register file.

## Slide 84: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg
Self Study
Notes: How does the forwarding work?
For simplicity, we consider only the challenge of forwarding to an operations in the EX stage, which may be either an ALU operation or an effective address calculation.
This means that when an instruction is trying to use the register in its EX usage than an earlier instruction intends to write in its WB stage, we actually need the values as inputs to the ALU.
(solution) A notation that names the fields of the pipeline registers allows for a more precise notation of dependences. E.g., “ID/EX.RegistersRs” refers to one of the register whose value is found in the pipeline register ID/EX, related to the first read port of the register file.

## Slide 85: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0
Finally, for an EX hazard we can have a forwarding unit which can check & do the following:
If (EX/MEM.RegWrite and (EX/MEM.RegRd ≠ 0) and (EX/MEM.RegRd = ID/EX.RegRs))
then ForwardA = 102
If (EX/MEM.RegWrite and (EX/MEM.RegRd ≠ 0) and (EX/MEM.regRd = ID/EX.RegRt))
then ForwardB = 102
Self Study

## Slide 86: Forwarding Paths

## Slide 87: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
Self Study

## Slide 88: Forwarding Conditions
FIGURE : The control values for the forwarding multiplexors
Summary of the control values for Mux:
Self Study

## Slide 89: Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true
Re-check

## Slide 90: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01
Self Study

## Slide 91: Datapath with Forwarding

## Slide 92: Load-Use Data Hazard
Need to stall for one cycle
As we have discussed before, the forwarding cannot save us when an instruction tries to read a register following a load instruction that writes the same register.
Thus, in addition to a forwarding unit, we need a hazard detection unit.
Notes: Note: As we have discussed before, the forwarding cannot save us when an instruction tries to read a register following a load instruction that writes the same register.
Thus, in addition to a forwarding unit, we need a hazard detection unit.

## Slide 93: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall (one cycle) and insert bubble, (after 1 cycle of stall forwarding will take care).
Make sure this is a ‘load’
Self Study
Notes: Note: The only instruction that reads from memory is the ‘load’.

## Slide 94: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  By instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 95: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 96: Datapath with Hazard Detection

## Slide 97: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Complier requires knowledge of the pipeline structure
The BIG Picture

## Slide 98: Control / Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)
7
Self Study
Notes: Figure shows a sequence of instructions and indicates when the branch would occur in this pipeline.
(Without any treatment) in our design and decision about whether to branch doesn’t occur until the MEM pipeline stage.
Compared to the data hazards this control or branch hazards are relatively simple to understand and they occur relatively less frequently.
There is nothing as effective against control hazards as forwarding is against data hazards.
We look at 2 schemes for resolving control hazards and one optimization to improve these schemes.

## Slide 99: Branch Hazards
§4.8 Control Hazards
Compared to the data hazards this control or branch hazards are relatively simple to understand and they occur relatively less frequently.
There is nothing as effective against control hazards as forwarding is against data hazards.
We look at 2 schemes for resolving control hazards and one optimization to improve these schemes.
Self Study

## Slide 100: Reducing Branch Delay
Move hardware to determine outcome to ID stage [ => reduce stall from 3 to 1 cycles]
  Target address adder
  Register comparator [XORing operands, then ORing results]
Example: branch taken
  36: sub $10, $4, $8 40: beq $1, $3, 7 44: and $12, $2, $5 48: or $13, $2, $6 52: add $14, $4, $2 56: slt $15, $6, $7 ... 72: lw $4, 50($7)
Self Study
Notes: Note:

## Slide 101: Example: Branch Taken
Self Study

## Slide 102: Example: Branch Taken
Self Study

## Slide 103: Reducing Branch Delay
Move hardware to determine outcome to ID stage [ => reduce stall from 3 to 1 cycles]
  Target address adder
  Register comparator [XORing operands, then ORing results]
If the branch is ‘NOT Taken’ then we do not even have this 1 cycle bubble or penalty.
Thus the assumption (prediction) of ‘Taken’ or ‘NOT Taken’ is better than waiting for the branch result and then to proceed.
We call this slot, which is possibly having 1 cycle penalty, a ‘Delayed Slot’.
Self Study
Notes: Note:

## Slide 104: Scheduling the branch delay slot
Self Study
Notes: Scheduling the branch delay slot.
The top box in each pair shows the code before scheduling; the bottom box shows the scheduled code.
In (a), the delay slot is scheduled with an independent instruction from before the branch. This is the best choice.
Strategies (b) and (c) are used when (a) is not possible. In the code sequences for (b) and (c), the use of $s1 in the branch condition prevents the add instruction (whose destination is $s1) from being moved into the branch delay slot. In (b) the branch delay slot is scheduled from the target of the branch; usually the target instruction will need to be copied because it can be reached by another path.
Strategy (b) is preferred when the branch is taken with high probability, such as a loop branch.
Finally, the branch may be scheduled from the not-taken fall-through as in (c).
To make this optimization legal for (b) or (c), it must be OK to execute the sub instruction when the branch goes in the unexpected direction. By “OK” we mean that the work is wasted, but the program will still execute correctly. This is the case, for example, if $t4 were an unused temporary register when the branch goes in the unexpected direction.

## Slide 105: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add $4, $5, $6
add $1, $2, $3
beq $1, $4, target
Can be resolved using forwarding
1st proceeding ins
2nd proceeding ins
3rd proceeding ins

## Slide 106: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add $4, $5, $6
lw $1, addr
beq $1, $4, target
1st proceeding ins
2nd proceeding ins

## Slide 107: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
lw $1, addr
beq $1, $0, target
1st proceeding ins

## Slide 108: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 109: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 110: 2-Bit Predictor
Only change prediction on two successive mispredictions
Notes: Note: 2 bit prediction is almost as good as n-bit predictor.

## Slide 111: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately
Self Study

## Slide 112: The final datapath and control

## Slide 113: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard
§4.9 Exceptions
Self Study

## Slide 114: Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Cause register
  We’ll assume 1-bit
    0 for undefined opcode, 1 for overflow
Jump to handler at 8000 00180
Self Study

## Slide 115: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined opcode: C000 0000
  Overflow: C000 0020
  …: C000 0040
Instructions either
  Deal with the interrupt, or
  Jump to real handler
Self Study

## Slide 116: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …
Self Study

## Slide 117: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware
Self Study

## Slide 118: Pipeline with Exceptions
Self Study

## Slide 119: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in EPC register
  Identifies causing instruction
  Actually PC + 4 is saved
    Handler must adjust
Self Study

## Slide 120: Exception Example
Exception on add in
  40 sub $11, $2, $4 44 and $12, $2, $5 48 or $13, $2, $6 4C add $1, $2, $1 50 slt $15, $6, $7 54 lw $16, 50($7) …
Handler
  80000180 sw $25, 1000($0) 80000184 sw $26, 1004($0) …
Self Study

## Slide 121: Exception Example
Self Study

## Slide 122: Exception Example
Self Study

## Slide 123: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!
Self Study

## Slide 124: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines
Self Study

## Slide 125: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP, 2 ways:
  1. Deeper pipeline
    To overlap more instructions  shorter clock cycle
  2. Multiple issue ( ~ is the name as well)
    Replicate pipeline stages  multiple pipelines; say 4 washers and 4 dryers instead of 1 each. But, all need to be busy.
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
    Modern high-end microprocessors attempt 3 to 6 IPC.
§4.10 Parallelism via Instructions
Notes: BIPS – billion instruction per second
From chapter 1: MIPS = (Clock rate / [CPI x 10^6]) => (4 x 10^9)/ ([1/4] x 10^6) = 16 x 10^3 MIPS = 16 BIPS.
CPI = ¼ (because 4 instructions per cycle) => IPC =4.

## Slide 126: Multiple Issue
Static multiple issue – [used at compile-time]
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue - [used at run-time]
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime
Self Study

## Slide 127: Speculation
~ one of the most important methods for more ILP
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing (‘roll-back’ adds complexity)
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated
Self Study
Notes: Note: The roll-back steps are the most challenging to design.

## Slide 128: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation
Self Study

## Slide 129: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load but the address it uses is not legal => exception! which should not have occurred without the speculative approach.
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)
Self Study

## Slide 130: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)
Self Study

## Slide 131: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with in a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary
Self Study

## Slide 132: MIPS with Static Dual Issue
Let’s consider MIPS with two-issue packets
  One is a integer ALU operation or, a branch instruction
  Other can be a load or, a store instruction
  64-bit aligned; so decoding 64 bit instructions
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU or branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load or store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU or branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load or store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU or branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load or store |  |  | IF | ID | EX | MEM | WB
Self Study

## Slide 133: MIPS with Static Dual Issue
Another 32 bits from IM,
2 more read ports and 1 more write port on the register file + another ALU
Assume, bottom ALU computes address for data transfer and the top ALU handles everything else.
Highlighted =>additional needs
for this dual issue.
Self Study

## Slide 134: Hazards in the Dual-Issue MIPS
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add $t0, $s0, $s1 load $s2, 0($t0)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required
Self Study

## Slide 135: Scheduling Example
Schedule this for static dual-issue MIPS
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
 | ALU/branch | Load/store | cycle
Loop: | nop | lw $t0, 0($s1) | 1
 | addi $s1, $s1,–4 | nop | 2
 | addu $t0, $t0, $s2 | nop | 3
 | bne $s1, $zero, Loop | sw $t0, 4($s1) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)
Self Study
Notes: Note: Just one pair (last row in the table) of instructions has both issue slots used.

## Slide 136: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name
Self Study
Notes: Note: Register renaming refers to a technique used to avoid unnecessary serialization of program operations due to the reuse of same registers. We remove the problem by changing the names of some of the registers.

## Slide 137: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at the cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi $s1, $s1,–16 | lw $t0, 0($s1) | 1
 | nop | lw $t1, 12($s1) | 2
 | addu $t0, $t0, $s2 | lw $t2, 8($s1) | 3
 | addu $t1, $t1, $s2 | lw $t3, 4($s1) | 4
 | addu $t2, $t2, $s2 | sw $t0, 16($s1) | 5
 | addu $t3, $t4, $s2 | sw $t1, 12($s1) | 6
 | nop | sw $t2, 8($s1) | 7
 | bne $s1, $zero, Loop | sw $t3, 4($s1) | 8
Check the simple example @Note-section below.
Self Study
Notes: (Important) Example: Let us see a simple example below:
=========================
Problem: Assume we are trying to add ‘3’ to all the array element (of integer).
Loop: a[i] = a[i] +3;
i=i+1;
Jump Loop;
--------------------------
MIPS code without loop unrolling:
Loop:
lw $t0, 0($t2)
addi $t0, $t0, 3 # stall is required before this!
sw $t0, 0($t2)
addi $s3, $s3, 1 # i= i +1
sll $t2, $s3, 2 # $t2= i * 4
j Loop
--------------------------
Now MIPS code with loop unrolling (unrolling 3 steps):
Loop:
lw $t0, 0($t2)
lw $t1, 4($t2)
lw $t3, 8($t2)
addi $t0, $t0, 3 # Now, not affected by the required stall from lw instruction, as an additional benefit!
addi $t1, $t1, 3
addi $t3, $t3, 3
sw $t0, 0($t2)
sw $t1, 4($t2)
sw $t3, 8($t2)
addi $s3, $s3, 3 # i= i +3
sll $t2, $s3, 2 # $t2= i * 4
j Loop
----------------------------------------------
Q: Why not unroll to large steps?
Ans: Cache misses will be relatively higher with the larger size of the loop-block => this penalty can reduce the effectiveness ultimately.

## Slide 138: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU
Self Study
Notes: Note: Dynamic multiple-issue processors are known as superscalar processors, or simply superscalars.

## Slide 139: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  lw $t0, 20($s2) addu $t1, $t0, $t2 sub $s4, $s4, $t3 slti $t5, $s4, 20
  Can start sub while addu is waiting for lw
Self Study

## Slide 140: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands
buffer
Self Study
Notes: Each functional unit has buffers, called reservation stations.

## Slide 141: Register Renaming
Reservation stations and reorder buffer (buffer in commit unit) effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required
Self Study
Notes: Register renaming refers to a technique used to avoid unnecessary serialization of program operations due to the reuse of same registers. We remove the problem by changing the names of some of the registers.

## Slide 142: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared
Self Study

## Slide 143: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards
Self Study

## Slide 144: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture
Self Study

## Slide 145: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W
Self Study

## Slide 146: ‘ARM Cortex A8’ and ‘Intel Core i7’ Pipelines
Processor | ARM A8 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 2 Watts | 130 Watts
Clock rate | 1 GHz | 2.66 GHz
Cores/Chip | 1 | 4
Floating point? | No | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 14 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | 2-level | 2-level
1st level caches/core | 32 KiB I, 32 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-1024 KiB | 256 KiB
3rd level caches (shared) | - | 2- 8 MB
§4.11 Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines
Self Study

## Slide 147: ARM Cortex-A8 Pipeline
The 1st 3 stages fetch instructions into 12-entry instruction fetch buffer.
The Address Generation Unit (AGU) uses Branch Target Buffer (BTB), Global History Buffer (GHB), and a Return Stack (RS) to predict branches to try keep the fetch queue full.
Instruction decode is of 5 stages and instruction execution is of 6 stages.
Self Study

## Slide 148: ARM Cortex-A8 Performance
Figure: CPI on ARM Cortex A8 for the Minnespec benchmarks, which are small versions of SPEC2000 benchmarks.
These benchmarks use the much smaller inputs to reduce running time by several orders of magnitude.
The smaller size significantly underestimates the CPI impact of the memory hierarchy (Ch 5).
Self Study

## Slide 149: Core i7 Pipeline
Self Study
Figure: The Core i7 pipeline with memory component.
The total pipeline depth is 14 stages, with branch mispredictions costing 17 clock cycles.
This design buffers 48 loads and 32 stores.
The 6 independent units can begin execution of a ready RISC operation each clock cycle.

## Slide 150: Core i7 Performance
Self Study
Figure: CPI of Intel Core i7 920 running SPEC2006 integer benchmarks.
Figure: Percentage of branch mispredictions and wasted work due to unfruitful speculation of intel Core i7 920 running SPEC2006 integer benchmarks.

## Slide 151: Matrix Multiply
Unrolled C code
1 #include <x86intrin.h>
2 #define UNROLL (4)
3
4 void dgemm (int n, double* A, double* B, double* C)
5 {
6 for ( int i = 0; i < n; i+=UNROLL*4 )
7 for ( int j = 0; j < n; j++ ) {
8 __m256d c[4];
9 for ( int x = 0; x < UNROLL; x++ )
10 c[x] = _mm256_load_pd(C+i+x*4+j*n);
11
12 for( int k = 0; k < n; k++ )
13 {
14 __m256d b = _mm256_broadcast_sd(B+k+j*n);
15 for (int x = 0; x < UNROLL; x++)
16 c[x] = _mm256_add_pd(c[x],
17 _mm256_mul_pd(_mm256_load_pd(A+n*k+x*4+i), b));
18 }
19
20 for ( int x = 0; x < UNROLL; x++ )
21 _mm256_store_pd(C+i+x*4+j*n, c[x]);
22 }
23 }
§4.12 Instruction-Level Parallelism and Matrix Multiply
Self Study

## Slide 152: Matrix Multiply
Assembly code:
1 vmovapd (%r11),%ymm4 # Load 4 elements of C into %ymm4
2 mov %rbx,%rax # register %rax = %rbx
3 xor %ecx,%ecx # register %ecx = 0
4 vmovapd 0x20(%r11),%ymm3 # Load 4 elements of C into %ymm3
5 vmovapd 0x40(%r11),%ymm2 # Load 4 elements of C into %ymm2
6 vmovapd 0x60(%r11),%ymm1 # Load 4 elements of C into %ymm1
7 vbroadcastsd (%rcx,%r9,1),%ymm0 # Make 4 copies of B element
8 add $0x8,%rcx # register %rcx = %rcx + 8
9 vmulpd (%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
10 vaddpd %ymm5,%ymm4,%ymm4 # Parallel add %ymm5, %ymm4
11 vmulpd 0x20(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
12 vaddpd %ymm5,%ymm3,%ymm3 # Parallel add %ymm5, %ymm3
13 vmulpd 0x40(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
14 vmulpd 0x60(%rax),%ymm0,%ymm0 # Parallel mul %ymm1,4 A elements
15 add %r8,%rax # register %rax = %rax + %r8
16 cmp %r10,%rcx # compare %r8 to %rax
17 vaddpd %ymm5,%ymm2,%ymm2 # Parallel add %ymm5, %ymm2
18 vaddpd %ymm0,%ymm1,%ymm1 # Parallel add %ymm0, %ymm1
19 jne 68 <dgemm+0x68> # jump if not %r8 != %rax
20 add $0x1,%esi # register % esi = % esi + 1
21 vmovapd %ymm4,(%r11) # Store %ymm4 into 4 C elements
22 vmovapd %ymm3,0x20(%r11) # Store %ymm3 into 4 C elements
23 vmovapd %ymm2,0x40(%r11) # Store %ymm2 into 4 C elements
24 vmovapd %ymm1,0x60(%r11) # Store %ymm1 into 4 C elements
§4.12 Instruction-Level Parallelism and Matrix Multiply
Self Study

## Slide 153: Performance Impact
Figure: Performance of 3 versions of DGEMM ( Double precision GEneral Matrix Multiply; continued from Ch 3) for 32 x 32 matrices.
AVX (Advanced Vector Extensions) are extensions to the x86 instruction set architecture.
Subword parallelism and instruction level parallelism has led to speedup of almost a factor of 9 over unoptimized code in chapter 3 (Figure 3.21).
Self Study

## Slide 154: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots
Self Study

## Slide 155: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls

## Slide 156: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks